## Slide 1: Computer Networks X_400487
Lecture 5
Chapter 4: Medium Access Control
Lecturer: Jesse Donkervliet
Includes slides from Vlad Cursaru

## Slide 2
IEEE 802.3
IEEE 802.11

## Slide 3: The MAC sublayer Medium Access Control
Lower part of the Data link layer.
Responsible for deciding who can use the communication channel.
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
You are here

## Slide 4: Didn’t we solve this at the Physical Layer???
A, video
B, video
C, www
D, email
A
B
C
D
Inefficient resource usage

## Slide 5: Didn’t we solve this at the Physical Layer???
A
B
C
D
A
B
C
D
…
Video streaming no longer works

## Slide 6: MAC Sublayer Outline
ALOHA & Slotted ALOHA
CSMA
1-persistent
nonpersistent
p-persistent
CSMA/CD
802.3 Ethernet
Ethernet Switching
MAC for Wireless
Hidden Terminal
Exposed Terminal
CSMA/CA
802.11 WiFi
Collision-Free Protocols
Basic Bit-Map
Token Ring
Binary Countdown

## Slide 7: Two Approaches: Contend or Coordinate
Contend
If there is data to send, send it!
Collisions are a fact of life.
Keep trying until sending succeeds.
Coordinate
If there is data to send, let other stations know.
Send when it is your turn.
Patiently wait while other stations are sending.
Protocols somewhere along the spectrum
Q: When to apply which strategy?

## Slide 9: ALOHA
In pure ALOHA, users transmit frames whenever they have data; if a collision occurs, users retry after a random delay.
M
M
M
Time
Stations
Q: When does ALOHA perform well/badly?
A
B
C
D
E
Collision
These stations use the same channel without mutiplexing on the physical layer.

## Slide 10: Collisions in ALOHA
M
M
Collision
Time

## Slide 11: Collisions in ALOHA
M
M
Collision
Time

## Slide 12: Collisions in ALOHA
Frame collisions can occur anywhere within 2 times duration of transmission.
M
M
Collision
Time
If another frame is sent anywhere in this period, a collision occurs

## Slide 13: Pure ALOHA
M
M
M
Time
Stations
All of these messages will have to be retransmitted!
Collisions
Q: How can we reduce the risk of collision?

## Slide 14: Slotted ALOHA
M
M
M
Time
Stations
These messages will have to be retransmitted!
First frame sent successfully
Probability of frame collisions is reduced. Frames now overlap completely, or not at all.

## Slide 15: Carrier Sense Multiple Access

## Slide 16: Carrier-Sense Multiple Access
Senders detect (“sense”) if the channel is in use
Protocols that apply CSMA:
1-persistent: wait for idle, then send. If collision, random back-off.
Nonpersistent: if busy, random back-off. Try again
-persistent: if busy, wait for next slot if idle, send with probability p

## Slide 17: 1-persistent CSMA
Wait until the channel is idle, then send
No
Send
Yes
Random back-off
Yes
Collision?
No
Channel free?
Q: Can you think of a problem with this method?

## Slide 18: Nonpersistent CSMA
Nonpersistent CSMA is less greedy. If the channel is occupied, it waits a random amount of time
Random back-off
No
Send
Yes
Yes
Collision?
No
Channel free?
Q: Can you think of a problem with this method?

## Slide 19: p-persistent CSMA
Keeps waiting. Sends frame with probability
Collision?
Yes
No
Skip slot
Applies to slotted channels.
No
Skip slot
Random back-off
No
Channel free?
Yes
Send
Yes
Channel free?
Yes
Send? (prob )

## Slide 20: Behavior of -persistent CSMA
Q: What trade-off do these protocols make?
Latency, bandwidth, (protocol) complexity
Early computer networks research evaluated protocol performance theoretically, using assumptions such as packet arrivals following Poisson distributions. Empirical research showed this not to be the case.* We still(!) lack mathematical tools to describe the behavior of these systems, and instead rely on observing the behavior of these systems “in the wild.”

## Slide 21: MAC Sublayer Outline
ALOHA & Slotted ALOHA
CSMA
1-persistent
nonpersistent
p-persistent
CSMA/CD
802.3 Ethernet
Ethernet Switching
MAC for Wireless
Hidden Terminal
Exposed Terminal
CSMA/CA
802.11 WiFi
Collision-Free Protocols
Basic Bit-Map
Token Ring
Binary Countdown

## Slide 22: CSMA/CD
Carrier Sense Multiple Access with Collision Detection

## Slide 23: CSMA/CD: CSMA with Collision Detection
Idea: when collision is detected, do not finish sending. Stop transmission instead.
Separates contention periods from transmission periods.
Contention period: check if it is safe to send data.
Transmission period: send data.
Saves time and bandwidth
Remember?

## Slide 24: Collision detection
frame
frame
frame
Abort transmission when collision is detected.
A station is transmitting
Afterwards, other stations try to claim the channel.
A station transmits. No collision, channel claimed.

## Slide 25: Collision detection
frame
frame
frame
Abort transmission when collision is detected.
Reduce contention period duration to improve throughput
Q: How do longer frames affect throughput? How about latency?

## Slide 26: MAC Sublayer Outline
ALOHA & Slotted ALOHA
CSMA
1-persistent
nonpersistent
p-persistent
CSMA/CD
802.3 Ethernet
Ethernet Switching
MAC for Wireless
Hidden Terminal
Exposed Terminal
CSMA/CA
802.11 WiFi
Collision-Free Protocols
Basic Bit-Map
Token Ring
Binary Countdown

## Slide 27: Medium Access Control Classic Ethernet

## Slide 28: Medium Access Control in … Classic Ethernet
Multiple machines sharing a single Ethernet connection.

## Slide 29: Medium Access Control in … Classic Ethernet
Multiple machines sharing a single Ethernet connection.
Q: Which MAC protocol should we use?
Newer versions of Ethernet (10-gigabit Ethernet and up) only support point-to-point full-duplex operation.

## Slide 30: Medium Access Control in … Classic Ethernet
Uses 1-persistent CSMA/CD.
Random delay (back-off) after collision is computed with Binary Exponential Back-off.
Station waits slots, where between and . is the number of failed attempts.
Failed Attempts | Maximum Delay | Random Delay Range
… | … | 
Failed Attempts | Maximum Delay | Random Delay Range
… | … | 
maxw = 0
collision = True
while collision:
w = random.randint(0, maxw)
collision = delayed_send(frame, w)
if collision:
maxw = maxw << 1
maxw = maxw | 1
Q: What happens if more than 2 stations are trying to send a frame?

## Slide 31: Ethernet performance
Q: What is more bandwidth efficient? Why?
Contention periods
frame
frame
frame
Small frames
frame
frame
frame
Large frames
Less time claiming channel  more time sending data
Q: Is there a trade-off here? Why?

## Slide 32: Classic Ethernet Collision detection
Collisions can occur and take as long as 2 to detect.
 is the time it takes to propagate over the Ethernet.
Leads to minimum packet size for reliable detection.
Ethernet
M
M
M
Transmission takes seconds.
Q: Does the detection latency cause a problem?

## Slide 33: Classic Ethernet Collision detection
Collisions can occur and take as long as 2 to detect.
 is the time it takes to propagate over the Ethernet.
Leads to minimum packet size for reliable detection:
Ethernet
M
M
Transmission takes seconds.
Q: Does the detection latency cause a problem?

## Slide 34: Ethernet frames
Frame format still used in modern versions of Ethernet.*
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
0-1500
Bytes: 8
6
6
2
0-46
4
*VLAN-aware packets from 802.1Q use a slightly modified header.

## Slide 35: Ethernet frames
Frame format still used in modern versions of Ethernet.*
Bit-sequence used to indicate start of frame.
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
0-1500
Bytes: 8
6
6
2
0-46
4
*VLAN-aware packets from 802.1Q use a slightly modified header.

## Slide 36: Ethernet frames
Frame format still used in modern versions of Ethernet.*
Source and destination addresses.
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
Q: Why needed over a single link?
0-1500
Bytes: 8
6
6
2
0-46
4
*VLAN-aware packets from 802.1Q use a slightly modified header.
Q: What is the name of this address? What is it assigned to?

## Slide 37: Ethernet frames
Frame format still used in modern versions of Ethernet.*
Type/length field:
Indicates to which network layer protocol the data should be sent.
Values less than 0x600 (1536) can be interpreted as length. (IEEE 802.3 only)
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
0-1500
Bytes: 8
6
6
2
0-46
4
*VLAN-aware packets from 802.1Q use a slightly modified header.

## Slide 38: Ethernet frames
Frame format still used in modern versions of Ethernet.*
Pad field:
Used if data causes frame to be less than the minimum frame length.
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
0-1500
Bytes: 8
6
6
2
0-46
4
*VLAN-aware packets from 802.1Q use a slightly modified header.

## Slide 39: Ethernet frames
Frame format still used in modern versions of Ethernet.*
32-bit Cyclic Redundancy Check used for error detection.
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
Q: How long is the generator polynomial?
0-1500
Bytes: 8
6
6
2
0-46
4
*VLAN-aware packets from 802.1Q use a slightly modified header.
Q: Reliable delivery?
Q: Error detection/correction?
No acks!

## Slide 40: Data Link Layer Switching

## Slide 41: Switching Classic Ethernet
A
B
C
D
Remember?

## Slide 42: Switching Classic Ethernet with Hubs
A
B
C
D
Hub

## Slide 43: Switching Classic Ethernet with ✨Switches✨
A
B
C
D
Switch
Same network topology, but MAC protocol no longer needed, if the channel is duplex!
Q: Do we still need MAC?

## Slide 44: Ethernet evolution From hubs to switches
Hub
Classic Ethernet
Fast Ethernet
Gigabit Ethernet
10-Gigabit Ethernet
…
Switch
All ports/ wires are always
connected

## Slide 45: Ethernet switch
Switch
Frame buffer
Hash table
C
Port #2
1
2
3
4
8
From: A
To: C
From: A
To: C
2. Look up destination
1. Placed in buffer
Q: Advantages of switches?
3. Send out on correct port

## Slide 46: Learning bridges Backwards learning
Hash table:
A:1
B:3
Switch
1
2
3
4
From: A
To: C
From: A
To: C
From: A
To: C
From: A
To: C
From: B
To: A
From: B
To: A

## Slide 47: Ethernet Wiring pattern
Switch
To ISP
Router
Switch
Switches can connect to other switches

## Slide 48: Learning bridges Topology with loops
Switch
To ISP
Router
Switch
Network contains a loop
Q: What kind of problem can this cause?

## Slide 49: Spanning tree Example
No direct loops
Switch
Switch
Switch
Switch
Switch

## Slide 50: Spanning tree Example
No direct loops
Only links in spanning tree are used. Others ignored
Switch
Switch
Switch
Switch
Switch

## Slide 51: Spanning tree algorithm As a poem
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree which must be sure to span.
So packets can reach every LAN.
First the Root must be selected
By ID it is elected.
Least cost paths from Root are traced
In the tree these paths are placed.
A mesh is made by folks like me
Then bridges find a spanning tree.
– Radia Perlman, 1985.
2
3
6
2
7
8
4
3
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Selected as root.
Nodes select shortest path to root.
Switch
Switch
Switch
Switch
Switch
Switch
Switch
Q: Which metric to use for link cost?

## Slide 52: Spanning tree algorithm As a poem
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree which must be sure to span.
So packets can reach every LAN.
First the Root must be selected
By ID it is elected.
Least cost paths from Root are traced
In the tree these paths are placed.
A mesh is made by folks like me
Then bridges find a spanning tree.
– Radia Perlman, 1985.
2
3
6
2
7
8
4
3
Selected as root.
Nodes select shortest path to root.
Switch
Switch
Switch
Switch
Switch
Switch
Switch
Remaining links not used!

## Slide 53: MAC Sublayer Outline
ALOHA & Slotted ALOHA
CSMA
1-persistent
nonpersistent
p-persistent
CSMA/CD
802.3 Ethernet
Ethernet Switching
MAC for Wireless
Hidden Terminal
Exposed Terminal
CSMA/CA
802.11 WiFi
Collision-Free Protocols
Basic Bit-Map
Token Ring
Binary Countdown

## Slide 54: Medium Access Control for Wireless Channels

## Slide 55: Properties of Wireless Channels Affect MAC Protocol Design
The good news: no more wires.
The bad news:
Nodes cannot detect collisions while sending. (you cannot talk and listen at the same time!)
Hidden and exposed terminals.
We cannot detect collisions while transmitting!

## Slide 56: MAC for Wireless Channels: No Collision Detection
Channel is free, I can send my frame to B
M
M
My frame is colliding, better stop sending!
A
B
C
D

## Slide 57: MAC for Wireless Channels: No Collision Detection
Bad news 1/2
Channel is free, I can send my frame to B
Outgoing signal too strong to detect collision
Collision not detected because incoming signal is orders of magnitude weaker than outgoing signal.
A
B
C
D

## Slide 58: MAC for Wireless Channels: Carrier Sense has Limited Range
Bad news 2/2
Channel is free, I can send my frame B
Range too short to detect channel is in use
M
M
Stations sense that channel is idle, but their range is too short to detect a transmitting hidden terminal.
A
B
C
D
Hidden Terminal

## Slide 59: MAC for Wireless Channels: Carrier Sense has Limited Range
Bad news 2/2
Channel is free, I can send my frame A
M
M
Stations sense that channel is in use, but the exposed terminal’s signal would not reach and interfere with the intended recipient.
Channel is in use, I cannot send my frame to D
There would be no collision at recipients
A
B
C
D
Exposed Terminal

## Slide 60: Multiple Access with Collision Avoidance (MACA)
Send RTS
An approach to solve the hidden terminal and exposed terminal problem.
Example: B wants to send to A.
B
A
C
D
Receive RTS
Receive RTS
Send CTS
Waiting
Did not receive CTS, so clear to send to D.

## Slide 61: CSMA/CA (Collision Avoidance)
Physical channel sensing.
Sense if the channel is in use. Wait for channel to become idle.
Virtual channel sensing.
Frames carry a Network Allocation Vector (NAV) that indicates the length of the exchange.
Wait for end of exchange.
Data + Ack

## Slide 62: CSMA/CA
Send
Yes
Select random
Yes
No
No
Channel free?
Skip slot
Starts with a back-off, regardless of collision
Countdown paused when other channel is occupied
Backoff by selecting and counting down .

## Slide 63: CSMA/CA Example
M
A
B
C
A
D
Ready
Ready
Ready
Wait
Wait
Backoff
M
A
Backoff
Wait
Backoff
M
Backoff complete
Backoff complete
Backoff
A to D
D to A
Backoff complete
Starts with a back-off, regardless of collision
Virtual channel sensing: B and C keep waiting after A is done sending its frame. Expecting Ack.

## Slide 64: MAC Sublayer Outline
ALOHA & Slotted ALOHA
CSMA
1-persistent
nonpersistent
p-persistent
CSMA/CD
802.3 Ethernet
Ethernet Switching
MAC for Wireless
Hidden Terminal
Exposed Terminal
CSMA/CA
802.11 WiFi
Collision-Free Protocols
Basic Bit-Map
Token Ring
Binary Countdown

## Slide 65: Medium Access Control in … 802.11
Stations cannot detect collisions while they occur.
Relies on ACKs to determine if collision occurred.
Can use RTS/CTS, but usually does not.
Instead uses a protocol called CSMA/CA. CA: Collision Avoidance.
If ACK is lost, sender assumes frame was lost; retransmits frame

## Slide 66: Core elements of CSMA/CA
Physical channel sensing.
Sense if the channel. Wait for channel to become idle.
Virtual channel sensing.
Frames carry a Network Allocation Vector (NAV) that indicates the length of the exchange.
Wait for end of exchange.
Data + Ack

## Slide 67: CSMA/CA
Send
Yes
Select random
Yes
No
No
Channel free?
Skip slot
Starts with a back-off, regardless of collision
Countdown paused when other channel is occupied
Backoff by selecting and counting down .

## Slide 68: CSMA/CA Example
M
A
B
C
A
D
Ready
Ready
Ready
Wait
Wait
Backoff
M
A
Backoff
Wait
Backoff
M
Backoff complete
Backoff complete
Backoff
A to D
D to A
Backoff complete
Starts with a back-off, regardless of collision
Virtual channel sensing: B and C keep waiting after A is done sending its frame. Expecting Ack.

## Slide 69: Power saving in 802.11
Multiple methods possible
Beacon frames
Automatic Power Save Delivery (APSD)
…
APSD example:
M
M
M
M
M
M
M
M
M
M

## Slide 70: 802.11 Infrastructure mode
Other networks

## Slide 71: 802.11 Ad-hoc networks
Q: Can you think of a (dis)advantage?

## Slide 72: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2

## Slide 73: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Available for other types of frames in future versions of the protocol.

## Slide 74: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Indicates a control, management, or data frame.

## Slide 75: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Indicates frames to and from the access points (distribution system) respectively.

## Slide 76: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Indicates that the sender will enter power save mode.

## Slide 77: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Indicates that the sender has more frames for the receiver.

## Slide 78: 802.11 frames
Version
To DS
From DS
Power Management
Type
More data
Protected
…
…
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Indicates that the data is encrypted.
WPA2 uses encryptions based on AES (Advanced Encryption Standard)
Authentication uses username+password (e.g., Eduroam), or only a password (e.g., your wireless network at home).

## Slide 79: 802.11 frames
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Stations use the duration to update their Network Allocation Vector (NAV).

## Slide 80: 802.11 frames
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Q: Why a third address?

## Slide 81: Access point forwards frame to recipient
Address 2
Source
Address 3
M
M
Address 1
Destination

## Slide 82: Access point forwards frame to recipient
Address 2
Source
Address 1
Destination
Address 3
M
M
Internet-connected router

## Slide 83: 802.11 frames
Data
Frame control
Address 1
Destination
Address 2
Source
Address 3
CRC
Duration
Seq
0-2312
Bytes:
2
6
6
6
4
2
2
Q: Why a third address?
Q: Reliable delivery?
Q: Error detection/correction?

## Slide 84: MAC Layer Summary
Multiplexing on the link layer
Contention and coordination
Centralized and decentralized protocols
Properties: bandwidth efficiency, latency, complexity.
Protocols and mechanisms
Carrier Sense
Collision Detection, 1-persistent, nonpersistent, p-persistent
Collision Avoidance, MACA, CSMA/CA
Collision-free protocols, Basic bitmap, Token ring, Binary countdown
Wireless Channels
Limited Radio Range
Hidden terminals and Exposed terminals
Switching
Routing on the link layer
No MAC protocol needed when used on full-duplex wired channels
Q: Why useful?
Q: Which is better?
Q: Why not used on wireless channels?
Q: How to know where to send frames?
A
B
C
D
No
Send
Yes
Random back-off
Yes
Collision?
No
Channel free?
T
T
T
T
T
T
Token 
M
M

## Slide 85: MAC Sublayer Outline
ALOHA & Slotted ALOHA
CSMA
1-persistent
nonpersistent
p-persistent
CSMA/CD
802.3 Ethernet
Ethernet Switching
MAC for Wireless
Hidden Terminal
Exposed Terminal
CSMA/CA
802.11 WiFi
Collision-Free Protocols
Basic Bit-Map
Token Ring
Binary Countdown

## Slide 86: Collision-Free Protocols
Instead of detecting collisions, why not prevent collisions?
Protocol examples:
Basic Bit-Map Protocol
Token Ring
Binary Countdown
Replacing contention with coordination

## Slide 87: The Basic Bit-Map Protocol
An example of a collision-free protocol.
Stations that want to transmit send a ‘1’ in their slot.
If a station wants to transmit, it sends a 1
Stations transmit their frames in order
Q: What is the efficiency of this protocol?
Frame from 0
1
Frame from 0
0
1
2
3
Frame from 3
Frame from 1
Frame from 3
Frame from 1
1
1
0
1
2
3
Contention slot takes 1 time unit
Sending frame takes contention slots
With stations,
Efficiency increases if frame size increases/contention slot size decreases ( increases)

## Slide 88: Token Ring
A collision-free protocol.
Similar to the basic bit-map protocol.
All stations send in a predefined order.
Station with token is allowed to send frame, pass on token
T
T
T
T
T
Physical network layout need not be a ring
T
Token 
A
B
C
D
T
Q: What is the efficiency of this protocol?
M
M

## Slide 89: Binary countdown
Q: What is the trade-off these protocols make?
overhead,
frame
0
1
0
frame
0
1
1
0
1
Station 0 (00)
Station 1 (01)
Station 2 (10)
Station 3 (11)
Example: Stations 0, 2, and 3 want to send a frame
frame
0
0
Station 2 gives up
Station 0 gives up. Higher numbered station wants to send.
Q: Disadvantage of this protocol?

## Slide 90: Computer Networks X_400487
Lecture 5
Chapter 4: Medium Access Control
Lecturer: Jesse Donkervliet
Includes slides from Vlad Cursaru

## Slide 91: Extra Slides

## Slide 92: Medium Access Control Bluetooth

## Slide 93: Bluetooth Protocol Stack
No fixed set of protocols. Instead, profiles define the set of protocols for a given application.
25 profiles, including headset, intercom, streaming audio, remote control, personal area network, and others.

## Slide 94: Bluetooth Protocol Stack
Radio
Link Control
(Baseband)
Applications
L2CAP
Service
discovery
RFcomm
…
Link Manager
Host-controller interface
Host-controller interface separates chip features from device features.

## Slide 95: Bluetooth Protocol Stack
Radio
Link Control
(Baseband)
Applications
L2CAP
Service
discovery
RFcomm
…
Link Manager
Host-controller interface
Headset Profile
Remote Control Profile
Different profiles for different types of applications.

## Slide 96: Medium Access Control in … Bluetooth
Radio layer
Uses adaptive frequency hopping in 2.4GHz band.
Link layer
TDM with timeslots for master and slaves.
Synchronous CO for periodic slots in each direction.
Asynchronous CL for packet-switched data.
Links undergo pairing (user confirms passkey/PIN) to authorize them before use.
Connectionless or connection-oriented depending on the application.
Q: How to prevent interference with 802.11?

## Slide 97: Medium Access Control in … Bluetooth
A Bluetooth network is called a piconet.
Secondaries may be asleep (parked) to save power.
P
S
S
S
S

## Slide 98: Bluetooth piconet
Two piconets can be bridged into a scatternet.
P
S
S
S
S
P
S
S
S
Secondary device used as bridge

## Slide 99: Bluetooth frames
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data

## Slide 100: Bluetooth frames
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Used to identify primary device.

## Slide 101: Bluetooth frames
Addr
Type
F
A
S
CRC
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Bits: 3 4 1 1 1 8
Header repeated three times

## Slide 102: Bluetooth frames
Addr
Type
F
A
S
CRC
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Used to identify secondary device.
Bits: 3 4 1 1 1 8
Header repeated three times

## Slide 103: Bluetooth frames
Addr
Type
F
A
S
CRC
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Identifies frame types such as SCO or ACL
Bits: 3 4 1 1 1 8

## Slide 104: Bluetooth frames
Addr
Type
F
A
S
CRC
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Buffer full. Secondary cannot receive more data.
Bits: 3 4 1 1 1 8

## Slide 105: Bluetooth frames
Addr
Type
F
A
S
CRC
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Piggybacked acknowledgement
Bits: 3 4 1 1 1 8

## Slide 106: Bluetooth frames
Addr
Type
F
A
S
CRC
Uses multiple types of frames, similar to 802.16.
Bits:
72 54 0-2744
Bluetooth frame (1x data rate)
Access code
Header
Data
Used for flow control.
Bits: 3 4 1 1 1 8
Q: What is the window size?

## Slide 107: Bluetooth frames
Addr
Type
F
A
S
CRC
Enhanced data rates send faster but for the same time.
Bits:
72 54 16 0-8184 2
Bluetooth frame (2x or 3x data rate)
Access code
Header
Data
Bits: 3 4 1 1 1 8
Guard/Sync
Trailer

## Slide 108: Medium Access Control RFID

## Slide 109: RFID Readers
Stationary reader
Mobile reader

## Slide 110: Medium Access Control in … RFID
RFID uses readers and tags. Reader in charge of medium access control. Tags reply to requests.
Tags have no battery. Use reader signal to power reply

## Slide 111: Medium Access Control in … RFID
RFID uses readers and tags. Reader in charge of medium access control. Tags reply to requests.
Tags have no battery. Use reader signal to power reply

## Slide 112: RFID communication example
Generation 2 Tag identification.
Reader sends query and sets slot structure.
Tags reply (RN16) in a random slot; may collide.
Reader asks one tag for its identifier. (ACK)
Process continues until no tags are left.
Q: Similar to a method we have seen last lecture?
Q
Query
QRepeat
Q
QRepeat
Q
R
A
EPC
QRepeat

## Slide 113: RFID request frame
RFID uses multiple types of frames. Example of a request-frame:
Bits:
4 1 2 1 2 2 1 4 5
Command
1000
DR
M
TR
Sel
Session
Target
Q
CRC

## Slide 114: RFID request frame
RFID uses multiple types of frames. Example of a request-frame:
Bits:
4 1 2 1 2 2 1 4 5
Command
1000
DR
M
TR
Sel
Session
Target
Q
CRC
Used to configure physical layer properties (e.g., data rate).

## Slide 115: RFID request frame
RFID uses multiple types of frames. Example of a request-frame:
Bits:
4 1 2 1 2 2 1 4 5
Used to keep track of which tag is identified by which reader.
Allows tags to reply to multiple readers is the same area.
Command
1000
DR
M
TR
Sel
Session
Target
Q
CRC

## Slide 116: RFID request frame
RFID uses multiple types of frames. Example of a request-frame:
Bits:
4 1 2 1 2 2 1 4 5
Limits random backoff values available to the tags.
Command
1000
DR
M
TR
Sel
Session
Target
Q
CRC
Tag responds in a slot between and