## Slide 1: Computer Networks X_400487
Lecture 7
Chapter 5: The Network Layer—Part 1
Lecturer: Jesse Donkervliet

## Slide 2: Recap Data Link Layer
Data link layer (partially) answers the following questions:
How create frames from bits/bytes?
How to detect/correct transmission errors?
How to efficiently multiplex frames from multiple stations over a single channel?
channel
…
Data Link
Physical
…
Data Link
Physical
MAC sublayer
Q: What kind of efficiency?

## Slide 3: Recap Data Link Layer
Data link layer (partially) answers the following questions:
How create frames from bits/bytes?
How to detect/correct transmission errors?
How to efficiently multiplex frames from multiple stations over a single channel?
MAC sublayer
Q: What kind of efficiency?
channel
…
Data Link
Physical
…
Data Link
Physical
Data Link
Physical
Q: What kind of device is this?
Bridge / Switch

## Slide 5: What Else Do We Need?
Data link layer not enough for a world-wide internet (=network of networks)
Switches not built for large networks (e.g., hash table size)
Protocols tailored to physical medium: bad idea to use one such protocol for all types of networks
Hashmap of all addresses requires very large memory. Searching memory reduces performance.
Q: How to solve this?
Add new layer of abstraction: the Network Layer

## Slide 6: The Network Layer
The network layer (partially) answers the following questions:
How to get from A to B?
How to connect multiple networks?
How to manage network resources?
  How to prevent network congestion?
  How to provide Quality of Service?
A
B
Lowest layer concerned with “end-to-end” delivery

## Slide 7: The Network Layer
Link
DSL
SONET
802.11
Ethernet
…
Heart of the networking model, together with the transport layer (next week)
Layers below it do not know about end-to-end delivery
Layers above it do not know about the topology of the network
Both layers above and below do not know about routing
*Although switching is similar to routing…
Application
HTTP
SMTP
RTP
DNS
…
TCP
UDP
Transport
Network
IP
ICMP
TCP/IP form the “narrow waist” of the Internet

## Slide 8: The Network Layer
Data Link
Physical
channel
Data Link
Physical
Data Link
Data Link
Network
Physical
Physical
Network
Network
Data Link
Physical
…
…
Router
Network layer provides new features through new protocols and a new device (the router)
Q: Why have Data Link and Physical Layer twice?
Router performs store-and-forward packet switching

## Slide 9: The Network Layer
The network layer (partially) answers the following questions:
How to get from A to B?
How to connect multiple networks?
How to manage network resources?
  How to prevent network congestion?
  How to provide Quality of Service?
A
B
Lowest layer concerned with “end-to-end” delivery
Today’s lecture
Next lecture

## Slide 10: Today’s Lecture
Routing Algorithms
Internetworking

## Slide 11: Routing
Finding a path through a network

## Slide 12: Important Properties for Routing
Correctness
Simplicity
Robustness
Stability
Fairness
Efficiency
These properties can (and often do) conflict with each other.

## Slide 13: How to find a route?
We will look at three key ideas:
Distance vector routing
Link state routing
Hierarchical routing

## Slide 14: Routing tables
For each packet, we need to know on which link to forward it.
For this we use a routing table
To | Distance | Line
A | 7 | A
B | 59 | A
C | 0 | -
D | 75 | E
E | 1 | E
F | 103 | E
Routing table for C.
We are station C
We are directly connected to A
If packet should go to D, minimum distance is 75. Forward to E

## Slide 15: Routing tables
For each packet, we need to know on which link to forward it
For this we use a routing table
To | Distance | Line
A | 7 | A
B | 59 | A
C | 0 | -
D | 75 | E
E | 1 | E
F | 103 | E
Routing table for C.
We are indirectly connected to B

## Slide 16: Distance Vector Routing
Distance vector A
A, 0
B, 1
C, 7
D, 152
E, 8
F, 110
Send your distance vector to your neighbors
Update your routing table based on incoming distance vectors
A
Links to other machines
To | Distance | Line
A | 7 | A
B | 59 | A
C | 0 | -
D | 75 | E
E | 1 | E
F | 103 | E
Routing table for C.
Distance from A to B is 1
Distance from C to A is 7
Q: How to update our routing table?
C

## Slide 17: Distance Vector Routing
Send your distance vector to your neighbors
Update your routing table based on incoming distance vectors
A
Distance vector A
A, 0
B, 1
C, 7
D, 152
E, 8
F, 110
To | Distance | Line
A | 7 | A
B | 59 8 | A
C | 0 | -
D | 75 | E
E | 1 | E
F | 103 | E
To | Distance | Line
A | 7 | A
B |  | A
C | 0 | -
D | 75 | E
E | 1 | E
F | 103 | E
Routing table for C.
Q: What can go wrong when using this algorithm?
Links to other machines
C

## Slide 18: Distance Vector Routing Good News Propagation
B
C
A
Distance vector A
A, -
B, 4
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 5
C, -
1000
4
1

## Slide 19: Distance Vector Routing Good News Propagation
B
C
A
Distance vector A
A, -
B, 4
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 5
C, -
1000
42
1

## Slide 20: Distance Vector Routing Good News Propagation
B
C
A
Distance vector A
A, -
B, 42
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 5
C, -
1000
42
1

## Slide 21: Distance Vector Routing Good News Propagation
B
C
A
Distance vector A
A, -
B, 42
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 53
C, -
1000
42
1

## Slide 22: Distance Vector Routing Bad News Propagation
B
C
A
Distance vector A
A, -
B, 4
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 5
C, -
1000
4
1

## Slide 23: Distance Vector Routing Bad News Propagation
B
C
A
Distance vector A
A, -
B, 4
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 5
C, -
1000
42000
1

## Slide 24: Distance Vector Routing Bad News Propagation
B
C
A
Distance vector A
A, -
B, 46
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 5
C, -
1000
42000
1

## Slide 25: Distance Vector Routing Bad News Propagation
B
C
A
Distance vector A
A, -
B, 46
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 57
C, -
1000
42000
1

## Slide 26: Distance Vector Routing Bad News Propagation
B
C
A
Distance vector A
A, -
B, 68
C, 1
Distance vector B
A, 4
B, -
C, 5
Distance vector C
A, 1
B, 57
C, -
1000
42000
1

## Slide 27: Count to infinity problem When machine fails
A
B
C
D
Distance vector B
A, 1
B, -
C, 2
D, 1
Distance vector D
A, 2
B, 1
C, 1
D, -
Distance vector C
A, 3
B, 2
C, -
D, 1

## Slide 28: Count to infinity problem When machine fails
A
B
C
D
Distance vector B
A, 999
B, -
C, 2
D, 1
Distance vector D
A, 2
B, 1
C, 1
D, -
Distance vector C
A, 3
B, 2
C, -
D, 1
Oh no, we cannot reach A!
We can still get there via D!

## Slide 29: Count to infinity problem When machine fails
A
B
C
D
Distance vector B
A, 3
B, -
C, 2
D, 1
Distance vector D
A, 2
B, 1
C, 1
D, -
Distance vector C
A, 3
B, 2
C, -
D, 1
We can still get there via D!
Let’s update our routing table.
D: All my neighbors have a path to A > 2!

## Slide 30: Count to infinity problem When machine fails
A
B
C
D
Distance vector B
A, 3
B, -
C, 2
D, 1
Distance vector D
A, 4
B, 1
C, 1
D, -
Distance vector C
A, 3
B, 2
C, -
D, 1
We can still get there via D!
Let’s update our routing table.
D: All my neighbors have a path to A > 2!

## Slide 31: Count to infinity problem When machine fails
A
B
C
D
Distance vector B
A, 5
B, -
C, 2
D, 1
Distance vector D
A, 4
B, 1
C, 1
D, -
Distance vector C
A, 5
B, 2
C, -
D, 1
We can still get there via D!
Let’s update our routing table.
D: All my neighbors have a path to A > 2!
This will go on for a while…

## Slide 32: Link state routing
Does not suffer from the count to infinity problem, but is more complex
Uses a shortest path algorithm
Routers only send packets with information about their direct neighbors
These packets are flooded over the network
Routers built an overview of the network using these packets and run a shortest path algorithm
Replaced distance vector routing in ARPANET in 1979

## Slide 33: Flooding link state packets
A
B
C
D
B can reach A and D with distance 1.
M
M
M
M
Q: What can go wrong?
Q: What can go wrong with sequence numbers?

## Slide 34: Link state routing Building a map of the network
2
1
This is us.
3
5
2

## Slide 35: Link state routing Building a map of the network
2
5
1
3
4
This is us.
2: I’m connected to 3, 4, and 5
5
2
1
3
9

## Slide 36: Link state routing Building a map of the network
2
7
5
6
1
3
4
This is us.
4: I’m connected to 2, 6, and 7
5
2
1
3
9
2
1

## Slide 37: Link state routing Building a map of the network
2
7
5
6
9
8
1
3
4
This is us.
1
5
3
9
1
2
1
10
5
3
Q: Which route to take from 1 to 7?
2
Packets addressed to 7 should be routed via 3!
Q: Which algorithm is used here?
2
3
6
7
9
10
: cost to node is .

## Slide 38: Hierarchical routing
Reducing routing table sizes for large networks.
A1’s RT size: 7 (all other nodes).
A1

## Slide 39: Hierarchical routing
Reducing routing table sizes for large networks.
A1’s RT size: 7 (all other nodes).
A
B
C
A1
A2
A3

## Slide 40: Hierarchical routing
Reducing routing table sizes for large networks.
A1’s RT size: 4 (A2, A3, B, C).
A
B
C
A1
A2
A3

## Slide 41: Today’s Lecture
Routing Algorithms
Internetworking
  Real-World Routing in and between Autonomous Systems
  Tunneling
  Packet fragmentation

## Slide 42: Internetworking
Getting packets to their destination across multiple networks
Q: Difference between a single network and a collection of networks?

## Slide 43: Internetworking
Challenges for sending packets end-to-end over multiple networks:
Technological
  Different protocols
  Different maximum packet sizes
  Different QoS guarantees
Political
  Different costs
  Privacy concerns
  Competition/disputes

## Slide 44: Structure of the Internet: A Network of Networks

## Slide 45: We’ve almost come full circle: A Hierarchical Topology
A multitree?

## Slide 47: Structure of the Internet: A Network of Networks
ISPs and (large) corporations are Autonomous Systems (AS)
Network of networks: yet another layer of abstraction
A large corporation using multiple points of attachment: multihoming
Peering points (or Internet eXchange Points [IXPs]) connect ISPs and backbones
Homes and small businesses connect to the Internet via ISPs

## Slide 48: Internetworking with Autonomous Systems
Involves two key ideas:
Routing inside an Autonomous System
  Intradomain routing. Uses an Interior Gateway Protocol
Routing between Autonomous Systems
  Interdomain routing. Uses an Exterior Gateway Protocol
We will look at the Open Shortest Path First (OSPF) protocol
We will look at the Border Gateway Protocol (BGP)

## Slide 49: Open Shortest Path First (OSPF)
Routing within an Autonomous System.
Uses a form of link state routing
Builds a graph representation of the network
Support multiple distance metrics (e.g., delay, physical distance)
Broadcast LANs modeled as node with zero-cost links
Example of an Interior Gateway Protocol

## Slide 50: Open Shortest Path First (OSPF)
Routing within an Autonomous System.
Uses a hierarchy called “areas” to manage large networks
For destinations not in area: go through backbone
Q: Why support hierarchical routing?
All areas connected to Area 0 (backbone)
Area border router exchanges summarized routing info between areas
Routers only know topology of the area they are in
Boundary routers connect to another AS.
Uses both an Interior and Exterior Gateway Protocol
Example of an Interior Gateway Protocol

## Slide 51: Border Gateway Protocol (BGP)
Routing between (large) independent networks.
Supports arbitrary policies put in place by ISPs, companies, organizations, etc.
Q: Can you think of examples of such policies?
Example of an Exterior Gateway Protocol
Autonomous Systems connect at IXPs
AS1 provides transit service
Stub networks do not need BGP: only one way to send outgoing packets

## Slide 52: Border Gateway Protocol (BGP)
Routing between (large) independent networks.
Uses a path vector protocol (form of distance vector routing)
Example of an Exterior Gateway Protocol
Routing based on policies
Examples:
Peer above transit
Hot potato routing
Shortest AS path
Path Vectors

## Slide 53: Connecting Networks with Different Protocols
If source and destination networks use different protocols, they cannot communicate.
Network A:
Uses ‘cars’ protocol.
Network C:
Uses ‘planes’ protocol.
Network B:
Uses ‘boats’ protocol.

## Slide 54: Tunneling
Network type B
If an intermediate network uses different protocols, they can communicate by tunneling.
source
destination
Network type A
Network type A
Q: Can you name a (dis)advantage?
Used to route IPv6 packets over IPv4 networks
Routers support both types of network!

## Slide 55: Business as usual Packets in packets in packets in …
Data wrapped in headers from multiple networking layers.
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals
T
data
N
data
d
L
L
data
d
d
data

## Slide 56: Tunneling Packets in packets in packets in …
Data wrapped in headers from multiple networking layers.
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals
T
data
data
N
data
d
data
d
N
d
L
L
data
d
d
d
Network-layer packet used as payload for other network-layer packet

## Slide 57: Packet fragmentation Transparent fragmentation
Packet size can be limited by hardware, software, protocols, law, etc.
Q: What can cause packet size limits?
M
M
M
M
M
M
Packet too large for link.
M
M
M
M
M
M
Q: Can you name a (dis)advantage?
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3

## Slide 58: Packet fragmentation Nontransparent fragmentation
Packet size can be limited by hardware, software, protocols, law, etc.
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Packet too large for link.
Q: Can you name a (dis)advantage?
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3
Used in IP!

## Slide 59: Avoiding packet fragmentation MTU discovery
Packet size can be limited by hardware, software, protocols, law, etc.
M
M
Packet too large for link.
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3
Packet too large. Try 3!

## Slide 60: Avoiding packet fragmentation MTU discovery
Packet size can be limited by hardware, software, protocols, law, etc.
Used in IP!
M
M
M
M
M
M
M
M
Packet too large for link.
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3
M
M
M
M
M
M
M
M
Q: Can you name a (dis)advantage?