## Slide 1: Computer Networks X_400487
Lecture 8
Chapter 5: The Network Layer—Part 2
Lecturer: Jesse Donkervliet

## Slide 2: Well done at the Midterm!

## Slide 3: ALL YOUR NETWORKS ARE BELONG TO IP!

## Slide 4
How to find a route between machines across the globe?
How do routers manage the addresses of all these machines?
How does IP carry data over the Internet?
How to prevent network congestion?
How to traverse networks with different protocols/properties/…
How to provide quality of Service?

## Slide 5
How to find a route between machines across the globe?
How do routers manage the addresses of all these machines?
How does IP carry data over the Internet?
How to prevent network congestion?
How to traverse networks with different protocols/properties/…
How to provide quality of Service?

## Slide 6: Quick Links for Today
IPv4
NAT
Subnets
Token Bucket

## Slide 7: The Internet Protocol (IP)
Network Layer Protocol

## Slide 8: Challenges Addressed by IPv4 Protocol Design
Error detection/correction
Preventing permanently looping packets
Globally identifying computers
Carrying packets over links with different size requirements

## Slide 9: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
Check the book for the detailed view!

## Slide 10: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
Q: What is the value of this field?

## Slide 11: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
Q: Why have this field?

## Slide 12: Challenges Addressed by IPv4 Protocol Design
Error detection/correction
Preventing permanently looping packets
Globally identifying computers
Carrying packets over links with different size requirements

## Slide 13: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
Q: Why have this field?
16 bit length field  packet size can reach 64KiB

## Slide 14: 802.3 802.1Q
Pri
CFI
VLAN ID
Data
Preamble
Destination
address
Source
address
T/L
P
CRC
0-1500
Bytes: 8
6
6
2
0-46
4
VLAN type > 1500, interpreted as type
802.3 Frame layout
802.1Q Frame modifications:
VLAN
Tag
2
2
Q: How do non-VLAN aware bridges handle these frames?
VLAN ID (color)
Maximum frame size differs across link-layer protocols!

## Slide 15: Packet fragmentation Transparent fragmentation
Packet size can be limited by hardware, software, protocols, law, etc.
Q: What can cause packet size limits?
M
M
M
M
M
M
Packet too large for link
M
M
M
M
M
M
Q: Can you name a (dis)advantage?
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3

## Slide 16: Packet fragmentation Nontransparent fragmentation
Packet size can be limited by hardware, software, protocols, law, etc.
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Packet too large for link
Q: Can you name a (dis)advantage?
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3
Used in IP!

## Slide 17: Avoiding packet fragmentation MTU discovery
Packet size can be limited by hardware, software, protocols, law, etc.
M
M
Packet too large for link
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3
Packet too large. Try 3!

## Slide 18: Avoiding packet fragmentation MTU discovery
Packet size can be limited by hardware, software, protocols, law, etc.
Used in IP!
M
M
M
M
M
M
M
M
Packet too large for link
Max packet size: 3
Max packet size: 10
Max packet size: 10
Path Maximum Transmission Unit (MTU): 3
M
M
M
M
M
M
M
M
Q: Can you name a (dis)advantage?

## Slide 19: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
Q: Why have this field?

## Slide 20: Challenges Addressed by IPv4 Protocol Design
Error detection/correction
Preventing permanently looping packets
Globally identifying computers
Carrying packets over links with different size requirements

## Slide 21: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
IPv4 does not use a CRC but a checksum.
Computed by adding all 16-bit half-words in the header

## Slide 22: Challenges Addressed by IPv4 Protocol Design
Error detection/correction
Preventing permanently looping packets
Globally identifying computers
Carrying packets over links with different size requirements

## Slide 23: IP version 4
Frame header
32 bits wide
Differentiated services
Total length
Identification
Fragment offset
Time to live
Header checksum
Source address
Destination address
Options
Protocol
Version
IHL
DF
MF
Q: What service does IP not provide?
Q: Why have this field?

## Slide 24: IPv4 addresses
IPv4 uses 32-bit addresses. Written in dotted decimal notation. Address 0x80D00297 is written as 128.208.2.151.
32-bit address gives billion addresses.
Q: How to route packets to these addresses with latencies in the order of milliseconds?
Reduce routing table sizes using hierarchical routing!

## Slide 26
This ‘Internet’ thing is getting quite popular…

## Slide 27: Network Address Translation (NAT)
Outside
Home
To ISP
Network Address Translation Box
How to let everybody go online with only addresses?
House/company has only one “external” IP address.
Q: No headers left in IP header. How to implement this?
Devices have their own “internal” IP address.

## Slide 28: Network Address Translation (NAT)
Outside
Home
= source address.
= destination address.
= NAT box address.
NAT Box
P
D
N
T
A
P
D
N
T
P
D
N
T
P
D
N
T
A
:
Q: How to send something back to ?
= NAT box table index.
= source port.
= destination port.
Q: Objections to this approach?

## Slide 29: Challenges Addressed by IPv4 Protocol Design
Error detection/correction
Preventing permanently looping packets
Globally identifying computers
Carrying packets over links with different size requirements

## Slide 30: IP version 6
Multiple improvements over IPv4.
Many more addresses!
Simplified header – improves bandwidth/latency.
Easier to add options in the header.
Improved security support.
Backported to IPv4

## Slide 31: IP version 6
IP version 4
Address size: 32 bits.
Dotted decimal notation: 192.31.20.46
Number of addresses:
IP version 6
Address size: 128 bits.
Hexadecimal notation: 8000::123:4567:89AB:CDEF
Number of addresses:
That’s a lot!

## Slide 32
Hit the 30% milestone in 2020!
Hit the 40% milestone in 2022!
Q: Why is it taking so long?

## Slide 33: Connecting Networks with Different Protocols
If source and destination networks use different protocols, they cannot communicate.
Network A:
Uses ‘cars’ protocol.
Network C:
Uses ‘planes’ protocol.
Network B:
Uses ‘boats’ protocol.

## Slide 34: Tunneling
Network type B
If an intermediate network uses different protocols, they can communicate by tunneling.
source
destination
Network type A
Network type A
Q: Can you name a (dis)advantage?
Used to route IPv6 packets over IPv4 networks
Routers support both types of network!

## Slide 35: Business as usual Packets in packets in packets in …
Data wrapped in headers from multiple networking layers.
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals
T
data
N
data
d
L
L
data
d
d
data

## Slide 36: Tunneling Packets in packets in packets in …
Data wrapped in headers from multiple networking layers.
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
signals
T
data
data
N
data
d
data
d
N
d
L
L
data
d
d
d
Network-layer packet used as payload for other network-layer packet

## Slide 37: IP version 6
Frame header
32 bits wide
Differentiated services
Flow label
Next header
Payload length
Source address
Destination address
Hop limit
Version

## Slide 38: IP version 6
Frame header
32 bits wide
Differentiated services
Flow label
Next header
Payload length
Source address
Destination address
Hop limit
Version
Value 0x06 to indicate IP version 6

## Slide 39: IP version 6
Frame header
32 bits wide
Differentiated services
Flow label
Next header
Payload length
Source address
Destination address
Hop limit
Version
“Time to live” renamed to “Hop limit”

## Slide 40: IP version 6
Frame header
32 bits wide
Differentiated services
Flow label
Next header
Payload length
Source address
Destination address
Hop limit
Version
Specifies transport layer protocol or extension header

## Slide 41: Addressing the Problem of Too Many Addresses to Route
Managing the size of routing tables

## Slide 42: Internet Protocol Prefixes and Subnets
Vrije Universiteit given a prefix. E.g., all IP addresses that match 37.60.x.y.
Example address: 37.60.194.64.
00100101.00111100.11000010.01000000
Prefix: 37.60.0.0/16 Subnet mask: 11111111.11111111.00000000.00000000
Network
Host
Address starts with 37.60?
If yes, route to VU.
16 bits used by network
Organizations can further subdivide their prefix to create subnets
Prefixes handed out by single organization: ICANN
Routing algorithms can calculate routes to prefixes, instead of to every individual address

## Slide 43: Internet Protocol - CIDR Classless InterDomain Routing
TU Delft
37.62.0.0/15
VU
37.60.0.0/16
UvA
37.61.0.0/16
00100101.00111110.00000000.00000000
00100101.00111100.00000000.00000000
00100101.00111101.00000000.00000000
37.62.0.0/15 – B
37.60.0.0/16 – B
37.61.0.0/16 – B
A
B
C
D
E
M

## Slide 44: Internet Protocol - CIDR Classless InterDomain Routing
TU Delft
37.62.0.0/15
VU
37.60.0.0/16
UvA
37.61.0.0/16
00100101.00111110.00000000.00000000
00100101.00111100.00000000.00000000
00100101.00111101.00000000.00000000
First 14 bits are all equal!
37.62.0.0/15 – B
37.60.0.0/16 – B
37.61.0.0/16 – B
A
B
C
D
E
M

## Slide 45: Internet Protocol - CIDR Classless InterDomain Routing
TU Delft
37.62.0.0/15
VU
37.60.0.0/16
UvA
37.61.0.0/16
00100101.00111110.00000000.00000000
00100101.00111100.00000000.00000000
00100101.00111101.00000000.00000000
First 14 bits are all equal!
37.60.0.0/14 – B
A
B
C
D
E
M
Reducing routing table size through route aggregation

## Slide 46: Longest Matching Prefix
Consider the following routing table:
An incoming IP packet carries the destination address 137.70.32.128. On which port is this packet forwarded? Assume that the router uses the longest matching prefix.
Prefix | Port | Binary
137.70.32.192/26 | A | 10001001.01000110.00100000.11000000
137.70.32.0/20 | B | 10001001.01000110.00100000.00000000
137.64.0.0/10 | C | 10001001.01000000.00000000.00000000
0.0.0.0/0 | D | 00000000.00000000.00000000.00000000
137.70.32.128
10001001.01000110.00100000.10000000

## Slide 47: Internet Control Message Protocol (ICMP)
Network Layer Protocol

## Slide 48: Internet Control Message Protocol (ICMP)
If something goes wrong, routers send these messages to senders.
Some examples:
Destination unreachable
Time exceeded
“Echo” and “echo reply”
Router advertisement/solicitation
Packet needs fragmentation / packet too big
Used by the program traceroute
Used by the program ping

## Slide 49: Dynamic Host Configuration (DHCP)
Network Layer Protocol

## Slide 50: Dynamic Host Configuration Protocol (DHCP)
P
D
N
T
A
?
DHCP packet. A machine without an IP address requests to get one assigned.
Somewhere, a DHCP server received the request and offers an available address.
MAC addresses are built into NICs. But network addresses are not.
Wait, what is my IP address?
DHCP discover
DHCP offer
Q: How to send DHCP offer back to machine without an address?
Used to configure other settings such as: network mask, addresses of default gateway, DNS, time servers, etc.

## Slide 51: Address Resolution Protocol (ARP)
Network Layer Protocol

## Slide 52: Address Resolution Protocol (ARP)
P
D
N
T
A
Q: Problems with this approach?
We do not know which value of and go together

## Slide 53: Address Resolution Protocol (ARP)
P
D
N
T
A
Q: Problems with this approach?
?
ARP packet. is asking which link layer device accepts messages for IP address .
Station replies with ARP packet containing its IP (and MAC) address.
ARP packets wrapped in Ethernet frames.
Request is broadcast over Ethernet.

## Slide 54: Network-Layer Resource Allocation

## Slide 55: Two Main Service Types
Connectionless service:
Connection-oriented service:
M
M
M
M
M
M
M
M
M
M
M
M
M
M
A
B
A
B

## Slide 56: Connectionless Service Datagrams
Routers use routing algorithms to decide where to send each packet individually.
Used by the Internet Protocol (IP).
M
M
M
M
M
M
M
A
B

## Slide 57: Connection-Oriented Service Virtual Circuits
Decide fixed route during connection setup.
All packets part of the connection follow this route.
Q: What kind of parameters are
negotiated during connection setup?
M
M
M
M
M
M
M
A
B
ISPs can use this on top of IP.

## Slide 58: Service comparison
Datagrams
Virtual Circuits
Router failures have low impact
No setup required
Easy congestion control
Easy Quality of Service guarantees
Packets contain full addressing information. Routers are stateless.
Packets contain VC number. Routers keep track of active VCs.
Complexity moved. No free lunch
The “best” service depends on your use case

## Slide 59
How to find a route between machines across the globe?
How do routers manage the addresses of all these machines?
How does IP carry data over the Internet?
How to prevent network congestion?
How to traverse networks with different protocols/properties/…
How to provide Quality of Service?

## Slide 60: Congestion control
Preventing traffic jams

## Slide 61: Looking back on flow control
Mechanism in data link layer.
Makes sure a sender does not send information faster than a receiver can accept.
Q: What can go wrong?
Q: Did we fix the issue?
Adding lots of buffer space.

## Slide 62: Congestion control
Combined responsibility of the network and transport layers.
Effective bandwidth
“Goodput”
Network load
Goodput: rate of useful packets arriving at the receiver
Network capacity
Ideal response
Desired response
Congestion collapse

## Slide 63: Approaches to congestion control
How can we fix this?

## Slide 64: Approaches to congestion control
Simplest approach is resource over-provisioning.
Preventing congestion by installing more bandwidth.
Can we do something smarter?

## Slide 65: Traffic-aware routing
If link costs are static, all traffic is routed over lowest-cost links.
2
7
5
6
9
8
1
3
4
1
5
3
9
1
2
1
10
5
3
2

## Slide 66: Traffic-aware routing
Using dynamic cost calculation can prevent congestion.
2
7
5
6
9
8
1
3
4
1
5
3
91
19
2
1
10
5
3
2

## Slide 67: Traffic-aware routing
Using dynamic cost calculation can prevent congestion.
2
7
5
6
9
8
1
3
4
1
5
3
91
19
2
1
10
5
3
2
Can you think of a problem with this approach?
Calculate link cost as a function of current load

## Slide 68: Traffic-aware routing
Using dynamic cost calculation can prevent congestion.
2
7
5
6
9
8
1
3
4
1
5
3
91
19
2
1
10
5
3
2
Can you think of a problem with this approach?
Calculate link cost as a function of current load

## Slide 69: Traffic-aware routing
Using dynamic cost calculation can prevent congestion.
Need to prevent oscillations.
Small cost updates.
Multiple paths.
2
7
5
6
9
8
1
3
4
1
5
3
91
19
2
1
10
5
3
2
Calculate link cost as a function of current load
Q: Can think of a (dis)advantage?

## Slide 70: Admission control
If there is congestion, new traffic has to wait!
Admission Control

## Slide 71: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
2
7
5
6
9
8
1
3
4

## Slide 72: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
Can you find a path that does not result in congestion?
2
7
5
6
9
8
1
3
4

## Slide 73: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
Can you find a path that does not result in congestion?
2
7
5
6
9
8
1
3
4

## Slide 74: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
Can you find a path that does not result in congestion?
2
7
5
6
9
8
1
3
4

## Slide 75: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
Can you find a path that does not result in congestion?
2
7
5
6
9
8
1
3
4

## Slide 76: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
Can you find a path that does not result in congestion?
2
7
5
6
9
8
1
3
4

## Slide 77: Admission control
Admission control allows a new traffic load only if the network has sufficient capacity.
Can you find a path that does not result in congestion?
Yes: allow traffic.
No: traffic must wait
2
7
5
6
9
8
1
3
4
Q: Can think of a (dis)advantage?

## Slide 78: Traffic throttling
Send messages in the opposite direction to explicitly indicate network congestion.
Most common implementation:
Set special bits in IP packet.
Inform sender of congestion through TCP.

## Slide 79: Traffic throttling End-to-end
Send back a ‘choke’ signal. When the source receives this packet, it slows down transmission.
Q: Can think of a (dis)advantage?
choke
choke
choke
Used in TCP/IP via Explicit Congestion Notification (ECN).
M
M
M
M
Overloaded!

## Slide 80: Traffic throttling Link-by-link
Send back a ‘choke’ signal. Every router that receives this packet slows down transmission.
choke
choke
choke
Q: Can think of a (dis)advantage?
M
M
M
M
Overloaded!

## Slide 81: Traffic Shaping
Regulating Network Resource Usage

## Slide 82: Looking back on flow control
Mechanism in data link layer.
Makes sure a sender does not send information faster than a receiver can accept.
Q: What can go wrong?
Q: Did we fix the issue?
Adding lots of buffer space.

## Slide 83: Congestion control
Combined responsibility of the network and transport layers.
Effective bandwidth
“Goodput”
Network load
Goodput: rate of useful packets arriving at the receiver
Network capacity
Ideal response
Desired response
Congestion collapse

## Slide 84: Approaches to congestion control
How can we fix this?

## Slide 85: Traffic shaping
Regulates rate and burstiness of data entering the network.
Traffic
shaping
Packets
Traffic flow
Host
Network
Challenge: limit available data data rate, but allow bursty traffic

## Slide 86: Traffic shaping Token bucket
Outgoing rate between and .
Average outgoing rate equal to .
Token Bucket
Bucket can store a limited number of tokens
Storage size also called
Tokens comes in at constant rate
Incoming token rate also called
Sending bytes requires tokens
Maximum sending rate also called
Maximum burst duration is seconds

## Slide 87: Traffic shaping Token bucket example
Bucket loses 1Mtokens every second.
Full bucket contains 16M tokens.
Maximum burst duration is 16 seconds.
Or: s.
Tokens comes in at 3 Mtokens/s
Incoming token rate also called
Machine wants to send 4 MB/s
Maximum sending rate also called
Maximum burst duration is seconds
Bucket can store 16M tokens
Storage size also called
Token Bucket
Q: What happens after 16s?

## Slide 88: Traffic Shaping in Cloud Networks
Traffic shaping being used in practice

## Slide 89: Traffic Shaping in Cloud Networks
Traffic shaping affecting performance

## Slide 90: Load shedding
For if all else fails. Choosing partial failure over total system failure.
Choosing partial failure over total system failure
Load Shedding

## Slide 91: Load Shedding Random Early Detection (RED)
Drop packets randomly if buffer space is almost full.
M
M
Almost overloaded!
Notices packet loss. Concludes network congestion. Slows down.
Sends an implicit signal to the sender: slow down!
Q: What happens now?

## Slide 92: Load shedding
Works if transmission errors are unlikely cause of packet loss.
Wireless channels (and other unreliable channels) need to solve transmission errors on the data link layer to hide them from network layer
Wired links are reliable (errors are unlikely)

## Slide 93: Quality of Service
Computer networks traditionally offer best-effort service
Tries to get data from A to B, but no promises
Q: How is this solved in practice?
Hosts provide reliable delivery using retransmissions
Q: What is the problem with this approach?
Does not work (well) for many applications:
We will revisit this problem in later lectures. It is interesting that we encounter this problem at the link layer, but do not have the abililty to solve it without help from higher layers.

## Slide 94: Quality of Service and its parameters
Bandwidth
Delay
Jitter
Packet loss
Maximum data rate. Measured in bits per second
Time it takes to get from source to destination
Variation in packet delay.
0 jitter means delay is constant
Probability of packets being dropped

## Slide 95: Different applications have different requirements
Bandwidth
Delay
Jitter
File sharing
Audio on demand
Video on demand
Telephony
Videoconferencing
Packet loss
A
B
strict requirement
A
B
weak requirement

## Slide 96: Different applications have different requirements
Delay
Jitter
Audio on demand
Video on demand
Telephony
Videoconferencing
Packet loss
Bandwidth
File sharing
A
B
strict requirement
A
B
weak requirement

## Slide 97: Different applications have different requirements
Bandwidth
Delay
File sharing
Video on demand
Telephony
Videoconferencing
Packet loss
Jitter
Audio on demand
A
B
strict requirement
A
B
weak requirement

## Slide 98: Different applications have different requirements
Delay
File sharing
Audio on demand
Telephony
Videoconferencing
Packet loss
Bandwidth
Jitter
Video on demand
A
B
strict requirement
A
B
weak requirement

## Slide 99: Different applications have different requirements
Bandwidth
File sharing
Audio on demand
Video on demand
Videoconferencing
Packet loss
Delay
Jitter
Telephony
A
B
strict requirement
A
B
weak requirement

## Slide 100: Different applications have different requirements
File sharing
Audio on demand
Video on demand
Telephony
Packet loss
Bandwidth
Delay
Jitter
Videoconferencing
A
B
strict requirement
A
B
weak requirement

## Slide 101: Quiz Time!
10-15(?) minutes
Correct answers without explanation do not get points!
Please do not use external resources, including:
ChatGPT (forget AI, use and train your RI [Real Intelligence!])
Anything on or via the Internet (the Web, chat apps, etc)
Answers from your neighbors
The book / slides

## Slide 102: Network Layer Summary
Networking
Routing Algorithms:
  Distance Vector
  Link State
  Hierarchical
Problem of scale: too many addresses
  Not enough address space (solved by IPv6)
  Routing tables too large (problem reduced by aggregation)
Network configuration
  Obtaining an address (DHCP)
  Looking up corresponding MAC address (ARP)
Internetworking
Different networks have different properties
Using a common protocol (IP).
Tunneling through networks with other protocols.
MLPS supports multiple protocols, for faster switching
Within Autonomous Systems (e.g., OSPF)
Between Autonomous Systems (e.g., BGP)
Resource Management
Connectionless and Connection-oriented approaches
Congestion Control (RED, ECN, etc.)
Traffic Shaping (Token Bucket, Leaky Bucket)