## Slide 1: Computer Networks X_400487
Lecture 10
Chapter 6: The Transport Layer—Part 2
Lecturer: Jesse Donkervliet

## Slide 2: Roadmap: Transport Layer
Transport layer responsibilities and challenges
Connection establishment and release
Revisiting reliable delivery and flow control
  Reliable delivery
  Flow control
Congestion control and bandwidth allocation
TCP and UDP

## Slide 3: The End-To-End Argument
If the network is unable to provide a feature by itself, it should be removed from the network and provided by the hosts.
The lower layers
Transport layer or higher
Q: Can you think of an example of a feature provided by the hosts?
Q: Can you think of a feature provided by the network?

## Slide 4: Error control in the transport layer
The transport layer is responsible for providing a reliable data stream over an unreliable network.
Q: Did we not take care of this in the data link layer?
Transport layer checks the end-to-end correctness of data.
Q: Why not do error control only at the transport layer?

## Slide 5: Reliable Delivery through Retransmissions
M0
time
M0
A1
M
M0
A1

## Slide 6: Improving Performance by using Error control on lower layers

## Slide 7: Error control and crash recovery
Protocol under normal circumstances.
time
Segment
Segment
ACK
Pass on to layer .
1
2
3
4

## Slide 8: Error control and crash recovery
Protocol when machines fail.
time
Segment
Segment
Pass on to layer .
1
2
3
ACK not transmitted!
Q: How to solve this?

## Slide 9: Crash recovery
Protocol under normal circumstances.
time
Segment
Segment
ACK
Pass on to layer .
1
3
2
4

## Slide 10: Error control and crash recovery
Protocol when machines fail.
time
Segment
Segment
ACK
1
2
3
Data not passed to next layer!

## Slide 11: Crash recovery on layer
We cannot create fool-proof crash recovery in layer .
Recovery from a layer crash can only be done by layer .
Q: What does this mean in practice?
When a crash occurs, the transport layer leaves it to the application layer to fix it!

## Slide 12: Roadmap: Transport Layer
Transport layer responsibilities and challenges
Connection establishment and release
Revisiting reliable delivery and flow control
  Reliable delivery
  Flow control
Congestion control and bandwidth allocation
TCP and UDP

## Slide 13: Regulating sending rate Flow control
Flow control is needed to slow down the sender if the receiver cannot handle the data rate
A
B
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Phone cannot handle high data rate
M
M
M
Small capacity receiver!

## Slide 14: Regulating sending rate Congestion control
Congestion control is needed to slow down the sender if the network cannot handle the data rate
A
B
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Network cannot handle high data rate
This can also happen when many users share the same links
Small capacity network!
M
M
M
M
M
M

## Slide 15: Stop-and-Wait: A 1-Bit Sliding Window Protocol
M
M
M
M
time
A
A
A
A
1-bit sliding window protocol

## Slide 16: Stop-and-Wait: A 1-Bit Sliding Window Protocol
M
M
A
A
M
M
time
A
A
1-bit sliding window protocol
Bandwidth inefficient for high-latency channels

## Slide 17: Sliding window protocols
Send multiple frames at the same time before waiting for an acknowledgement. (i.e., filling the pipe)

## Slide 18: Recap: Link Utilization
It takes seconds to send frame,
It takes D s for the frame to arrive at the receiver, takes D s for the (0-bit) acknowledgment to come back at the sender
1 frame per seconds
Frame size (in bits/bytes):
Window size (in frames):
Bandwidth (max. data rate of physical channel):
Bandwidth (frames per second):
Propagation delay (in seconds):
B Mbps network
Link utilization=
M
A
M
time
A
M

## Slide 19: Flow control and buffer management
Received packets have to be buffered at the receiver.
Perform buffer management separately. Use available buffer space as the receiver window size.
Q: Why do we need this?
Used by TCP!
buffer
M
buffers available
M
buffers available
Piggybacked!
We have to wait for the application to read the data
Limit window size to

## Slide 20: Roadmap: Transport Layer
Transport layer responsibilities and challenges
Connection establishment and release
Revisiting reliable delivery and flow control
Congestion control and bandwidth allocation
TCP and UDP

## Slide 21: Today
Congestion Control in TCP/IP
DNS
Email
Quiz?!

## Slide 22: Congestion control
Both the network layer and the transport layer are responsible for congestion control.
The transport layer controls the workload; implements congestion control and flow control by reducing sending rate.
Goodput
Network load
Network capacity
Ideal response
Desired response
Congestion collapse
Delay
Network load
Congestion collapse
Both packet loss and end-to-end delay can be used to signal congestion!

## Slide 23: Congestion control requires resource management
Congestion occurs if the workload is too large for the available network resources.
The workload of all users combined should not be too large for the available network resources.
Coordinate to divide network resources

## Slide 24: Fair bandwidth allocation
How to divide the available bandwidth over multiple senders?
Assume that we wave a total bandwidth and machines.
Q: How much bandwidth does each machine get?
May be impossible to implement with overlapping paths!
N = 3
Does not fit on link!
Bandwidth = 1
Bandwidth = 1
B = 2

## Slide 25: Fair bandwidth allocation Max-min fairness
Maximizes minimum bandwidth, then uses excess bandwidth where possible.
B = 2
N = 3
Q: Is this bandwidth allocation max-min fair?
No, because we can increase the minimum bandwidth.
Q: What is the downside of this method?

## Slide 26: Fair bandwidth allocation Convergence
When new connections enter the network, the bandwidth needs to be reallocated.
Bandwidth
time
Max bandwidth
Gray starts transmitting
Orange starts transmitting
Ideal scenario. In practice, convergence takes more time.
Q: Why is that?

## Slide 27: Available bandwidth is unknown
The transport layer is not aware of the network topology, or who else is using the network.
Because there is no centralized control, we need to dynamically adjust bandwidth usage using trial and error.
Q: Why is this the case?
Q: How to solve this problem?
Network

## Slide 28: Dynamically adjust bandwidth using trial and error
Max bandwidth
time
Yes!
No!
Keep trying to increase bandwidth usage.
Slow down when you receive congestion signal.
Alice’s bandwidth
Can we send use this much bandwidth?

## Slide 29: Sharing bandwidth example
Bob
Alice

## Slide 30: Sharing bandwidth example
Alice’s bandwidth
Bob’s bandwidth
Alice has 100% bandwidth Bob has 0% bandwidth
Alice has 0% bandwidth Bob has 100% bandwidth
Both use 0% bandwidth
Network not used
Both use 100% bandwidth
Network congestion (total 200%)

## Slide 31: Sharing bandwidth Efficiency and fairness
0%
100%
100%
Efficiency line
(sum is 100%)
Fairness line
(Alice and Bob have equal bandwidth)
Optimum
Bob’s bandwidth
Alice’s bandwidth

## Slide 32: Regulating sending rate Approaches
Multiple approaches to increase/decrease sending rate:
Additive (rate , rate ).
Multiplicative (rate , rate ).
Combination of both:
  Additive increase, additive decrease.
  Additive increase, multiplicative decrease.
  Multiplicative increase, additive decrease.
  Multiplicative increase, multiplicative decrease.
Q: Which one should we use?

## Slide 33: Additive increase Additive decrease
0%
100%
100%
Efficiency line
(sum is 100%)
angle 45
Q: What happens if we use this approach?
A: 80, B: 10 sum: 90
A: 90, B: 20 sum: 110
A: 80, B: 10 sum: 90
A: 90, B: 20 sum: 110
…
Below 100% bandwidth utilization No congestion

## Slide 34: Multiplicative increase Multiplicative decrease
0%
100%
100%
Efficiency line
(sum is 100%)
Below 100% bandwidth utilization No congestion
Vector from origin
Q: What happens if we use this approach?
A: 80, B: 10 sum: 90
A: 120, B: 15 sum: 135
A: 80, B: 10 sum: 90
A: 120, B: 15 sum: 135
…

## Slide 35: Regulating sending rate Efficiency and fairness
0%
100%
100%
Efficiency line.
(sum is 100%)
Additive increase/decrease
Multiplicative increase/decrease
Additive Increase Multiplicative Decrease (AIMD) converges to optimum
Decrease:
Increase:
Bob’s bandwidth
Alice’s bandwidth
A: 80, B: 10 sum: 90
A: 90, B: 20 sum: 110
A: 45, B: 10 sum: 55
A: 55, B: 20 sum: 75
A: 65, B: 30 sum: 95
A: 75, B: 40 sum: 115
A: 37, B: 20 sum: 57
Converges

## Slide 36: Additive increase Multiplicative decrease
Additive increase
Multiplicative decrease
0%
100%
100%
AIMD converges to / oscillates around optimum

## Slide 37: Regulating sending rate Efficiency and fairness
0%
100%
100%
Decrease:
Increase:
Bob’s bandwidth
Alice’s bandwidth
Q: What happens if bob uses another protocol such as UDP?
Use TCP-friendly protocols to prevent unfair competition

## Slide 38: Roadmap: Transport Layer
Transport layer responsibilities and challenges
Connection establishment and release
Revisiting reliable delivery and flow control
Congestion control and bandwidth allocation
TCP and UDP

## Slide 39: Internet protocols
The protocols that make the internet work.
Most popular on the transport layer:
UDP
TCP
But others exist!
You can create your own!
May not meet your application’s requirements!
All or
Nothing
Insufficient separation between mechanism and policy

## Slide 40: Comparing complexity by number of RFCs
UDP:
TCP:
RFC 1122
RFC 793
RFC 768
RFC 1323
RFC 2018
RFC 2581
RFC 2873
RFC 2988
RFC 3168
RFC …
RFC …
Overview of RFCs in RFC 4614.
…
Request For Comment (RFC) are published by the Internet Engineering Task Force (IETF).

## Slide 41: User Datagram Protocol (UDP)
Very thin layer on top of IP. Header provides ports needed to connect to remote applications.
u
Source port
Destination port
UDP length
UDP checksum
The UDP header
32 bits
RFC 768

## Slide 42: User Datagram Protocol (UDP)
Very thin layer on top of IP. Header provides ports needed to connect to remote applications.
UDP does not do:
Flow control
Congestion control
Retransmissions
Source port
Destination port
UDP length
UDP checksum
The UDP header
32 bits
Includes fields from the IP header!
Q: Can you name a service that works well with UDP?
RFC 768

## Slide 43: Transmission Control Protocol (TCP)
One of the most important protocols on the internet.
Provides a reliable end-to-end byte stream over an unreliable network.
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)

## Slide 44: Transmission Control Protocol (TCP)
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)
Sequence numbers and acknowledgements allow reliable, in-order delivery and enable sliding window protocols

## Slide 45: Transmission Control Protocol (TCP)
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)
TCP checksum uses same IP-header fields as the UDP checksum

## Slide 46: Transmission Control Protocol (TCP)
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)
Q: How do we know how long the TCP segment is?

## Slide 47: Transmission Control Protocol (TCP)
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)
Q: Used for flow control or congestion control?

## Slide 48: Connections in TCP

## Slide 49: Transmission Control Protocol (TCP)
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)
Used to establish/release connections

## Slide 50: TCP connection establishment Three-way handshake
Every data byte has its own sequence number.*
*SYN and FIN also have their own sequence numbers.
time
Connection request SYN (seq=x)
SYN, ACK (seq=y, ack=x+1)
ACK (seq=x+1, ack=y+1)
Sequence number x+1: bytes 0 to x have been received. Expecting byte x+1 next
Uses timestamp option to improve performance on high-bandwidth networks
Initial sequence numbers are randomly generated

## Slide 51: TCP Timestamp Option
Source port
Destination port
header length
TCP checksum
The TCP header
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Data (optional)
32 bits
Options (0 or more 32-bit words)

## Slide 52: TCP Timestamp Option
Use seq. number + timestamp to detect duplicates
Source port
Destination port
header length
TCP checksum
The TCP header
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
kind=8
Data (optional)
32 bits
length=10
timestamp value …
… timestamp value
timestamp echo reply …
… timestamp echo reply
Q: How does this improve performance?

## Slide 53: TCP PAWS

## Slide 54: TCP sequence numbers
Every data byte has its own sequence number
time
ACK (seq=x, ack=y)
ACK (seq=y, ack=x+len(a1))
ACK (seq=x+len(a1), ack=y+len(b1))
Initial sequence numbers are randomly generated
A1
B1
A2

## Slide 55: TCP connection release Two simplex channels
Every data byte has its own sequence number.*
*SYN and FIN also have their own sequence numbers.
time
Connection release: FIN, ACK (seq=x, ack=y)
ACK (seq=y, ack=x+1)
ACK (seq=x+1, ack=y+2)
FIN, ACK (seq=y+1, ack=x+1)

## Slide 56: TCP connection release Two simplex channels
Every data byte has its own sequence number.*
*SYN and FIN also have their own sequence numbers.
time
Connection release:
FIN, ACK (seq=x, ack=y)
FIN, ACK (seq=y, ack=x+1)
Q: How to solve the two army problem?
ACK (seq=x+1, ack=y+1)

## Slide 57: Error Control in TCP

## Slide 58: Reliable Delivery through Retransmissions
M0
time
M0
A1
M
M0
A1

## Slide 59: Setting Retransmission Timers
How long should we wait before retransmitting a frame?
Timer must be longer than round-trip time.
If we set timer too high, bandwidth efficiency goes down
Q: What are the bounds?
Congestion makes round-trip time variable!

## Slide 60: Dynamic Timeouts in TCP
Use a weighted moving average to smooth round trip time (R):
Do the same for the round trip time variance (RTTVAR):
Calculate new retransmission timeout (RTO) based on these values:

## Slide 61: Performance improvement Fast retransmission
Packet loss detected when timers expire.
Takes time (by design)!
time
Segment
Segment
ACK
Segment
ACK
Q: Can we know about packet loss before the timer runs out?
Duplicate acknowledgments can indicate packet loss
Q: Assumption?

## Slide 62: Flow Control in TCP

## Slide 63: Flow control and buffer management
Received packets have to be buffered at the receiver.
Perform buffer management separately. Use available buffer space as the receiver window size.
Q: Why do we need this?
Used by TCP!
buffer
M
buffers available
M
buffers available
Piggybacked!
We have to wait for the application to read the data

## Slide 64: TCP window size Flow control
time
2K data, seq 1
Ack 2K+1, win 2K
2K data, seq 2K+1
The window size tells sender how much data the receiver can handle.
Ack 4K+1, win 0
Ack 4K+1, win 2K
Q: Can you think of a potential problem?

## Slide 65: TCP window size Nagle’s algorithm
A sender that produces data in small amounts.
time
1 byte data, seq 1
Ack 2, win 2047
Small segments cause large overhead
1 byte data, seq 2
Ack 3, win 2046
Do not send more than one small packet at a time: wait for ack
Q: Can you think of an application that does this?
Q: For which applications may this not work well?

## Slide 66: TCP window size Silly-window syndrome
A receiver that consumes data in small amounts.
time
Ack 1, win 1
1 byte data, seq 1
Ack 2, win 0
Tiny window sizes cause large overhead
Ack 2, win 1
1 byte data, seq 2
Do not send window updates if available space is too small

## Slide 67: TCP Delayed Acknowledgements
Wait up to 500 ms to send acknowledgement
Send acknowledgement for every second full-size segment
time
100 bytes data, seq 1
ack 101
Try to improve bandwidth efficiency (e.g., through piggy-backing)
500 ms timer
500 bytes data, seq 1,

## Slide 68: TCP Delayed Acknowledgements
Wait up to 500 ms to send acknowledgement
Send acknowledgement for every second full-size segment
time
536 bytes data, seq 1
ack 1073
Try to improve bandwidth efficiency (e.g., through piggy-backing)
500 ms timer
536 bytes data, seq 537

## Slide 69: Congestion Control in TCP

## Slide 70: Transmission Control Protocol (TCP)
Source port
Destination port
header length
TCP checksum
The TCP header
32 bits
CWR
ECE
ACK
SYN
FIN
Sequence number
Acknowledgement number
Window size
Urgent pointer
Options (0 or more 32-bit words)
Data (optional)
Used for Explicit Congestion Notification

## Slide 71: Additive increase multiplicative decrease in TCP
AIMD used to prevent network congestion. Converges to fair and efficient bandwidth allocation.
TCP implements this using its congestion window.
Not the same as the ‘window size’ field in the TCP segment header!
Q: How does TCP combine the two windows?
Congestion window is tracked on the sender.
Specifies how many segments can be transmitted.

## Slide 72: AIMD in TCP What value to start with?
We want fast convergence, but sending a large burst can occupy low-bandwidth links for a long time.
Increase congestion window whenever acknowledgements arrive.
Alice
Low bandwidth
M
M
M
M
M
M
A
A
A
A
A
A
Acknowledgement rate tells us data rate of slowest link.

## Slide 73: AIMD in TCP ‘slow’ start
time
data
ack
Previous algorithm used congestion window = flow control window.
Slow start is slower in comparison
Q: What kind of growth does this cause?
Congestion window size grows based on acknowledgment rate

## Slide 74: TCP ‘slow’ start
Arbitrary threshold switches from ‘slow’ start to additive increase.
Congestion window
(KB or packets)
Transmission round (RTTs)
Congestion window growing over time
Slow start
Threshold
Current window

## Slide 75: TCP Tahoe
Arbitrary threshold switches from ‘slow’ start to additive increase.
Congestion window
(KB or packets)
Transmission round (RTTs)
Threshold
Threshold
multiplicative decrease
(thresholdwindow)
Additive increase
Current window
Packet loss detected
Reset congestion window
Wait 1 RTT for segments to leave the network
Q: Can you think of another way to detect packet loss?

## Slide 76: Performance improvement Fast retransmission
Packet loss detected when timers expire.
Takes time (by design)!
time
Segment
Segment
ACK
Segment
ACK
Q: Can we know about packet loss before the timer runs out?
#packets in transit
1
0
1
2
1
We can count the number of packets in the network!

## Slide 77: TCP Reno (= TCP Tahoe + fast recovery)
Current window
Congestion window
(KB or packets)
Transmission round (RTTs)
multiplicative decrease
(thresholdwindow)
Packet loss detected
Calculates the number of segments in the network by counting the number of duplicate acknowledgements
Threshold
Threshold
Fast recovery
Threshold reduced using multiplicative decrease.
Congestion window set to new threshold value.

## Slide 78: What about Explicit Congestion Notification?
M
M
M
M
M
M
= regular IP packet with TCP segment
= Explicit Congestion Notification (ECN) set in IP header
Congested Router

## Slide 79: What about Explicit Congestion Notification?
M
M
M
M
M
M
M
= regular IP packet with TCP segment
= Explicit Congestion Notification (ECN) set in IP header
= ECN-Echo (ECE) set in TCP header

## Slide 80: What about Explicit Congestion Notification?
M
M
M
M
M
M
M
= regular IP packet with TCP segment
= Explicit Congestion Notification (ECN) set in IP header
= ECN-Echo (ECE) set in TCP header
M
= Congestion Window Reduced (CWR) set in TCP header

## Slide 81: Different Flavors of TCP

## Slide 82: TCP versions and congestion signals
TCP determines rate based on packet loss.
CUBIC TCP determines rate based on packet loss.
FAST TCP determines rate based on end-to-end delay.
Compound TCP determines rate based on end-to-end delay and packet loss.
TCP with Explicit Congestion Notification.
XCP explicitly tells sender what rate to use.
Used by default in Linux, Windows, MacOS

## Slide 83: TCP versions and congestion signals
TCP determines rate based on packet loss.
CUBIC TCP determines rate based on packet loss.
FAST TCP determines rate based on end-to-end delay.
Compound TCP determines rate based on end-to-end delay and packet loss.
TCP with Explicit Congestion Notification.
XCP explicitly tells sender what rate to use.
Implicit congestion signals
Used by default in Linux, Windows, MacOS

## Slide 84: Roadmap: Transport Layer
Transport layer responsibilities and challenges
Connection establishment and release
Revisiting reliable delivery and flow control
Congestion control and bandwidth allocation
TCP and UDP

## Slide 85: Transport Layer Summary
Sockets interface
Connection establishment and release
  Duplicate detection
  Two army problem
Seq. num wrap around + duplicate detection  performance limit
End-to-end argument
Error control
  Timer management
  Detection using time-outs or duplicate acknowledgements
Flow control
  Sending rate limited to smallest window size
  Nagle’s algorithm
  Silly window syndrome
Congestion control
  Sharing available resources
    AIMD
  Multiple signals: packet loss, latency, etc.