## Slide 1: Computer Networks X_400487
Lecture 3
Chapter 3: The Data Link Layer—Part 2
Lecturer: Jesse Donkervliet

## Slide 2: Data Link Layer — Roadmap
Part 1
Framing
Flow Control
Guaranteed Delivery
Sliding Window Protocols
Part 2
Error detection
Error correction

## Slide 3
A single bit flip can break these images
1 Gibibyte = bits

## Slide 4: Error Detection

## Slide 5: Detecting errors in received frames
Data at sender: 0111010101010111010001
Data at receiver: 0111010111010111010001
Somehow bit was flipped!
Q: What causes these bit flips?

## Slide 6: Adding redundant bits
For a message of bits, send an extra redundant bits.
Send to the receiver.
Systematic code
Data (m bits)
Check bits (r bits)
Codeword (m+r bits)

## Slide 7: Hamming distance
Number of bits that differ between two bit strings.
10001001
10110001
Hamming distance 3.
110 111 101 001
Three bit flips required to change from one sequence to the other.
Adding redundant bits increases the distance between valid bit strings!

## Slide 8: How many errors can we detect?
Consider code words:
000111
111111
000000
Hamming distance , so we can detect single-bit errors.
000111 111111
Q: How many single-bit errors can we detect?

## Slide 9: Error detection
Linear, systematic block codes:
Parity
Checksums
Cyclic Redundancy Checks (CRCs)
Block is bits large
Important code properties:
Code Rate:
Number of errors reliably detected: N
Q: How to assess the quality of these codes?

## Slide 10: Parity
Add single bit such that:
The sum of the data bits modulo 2 is 0.
The number of 1’s is even.
Send example: 1110000 11100001
Receive example: 11010101
Easy to detect an odd number of errors.
Q: How many bit errors can be detected?
Error detected!

## Slide 11: Parity
Add single bit such that:
The sum of the data bits modulo 2 is 1.
The number of 1’s is odd.
Send example: 1110000 11100000
Receive example: 11010100
Easy to detect an odd number of errors.
Q: How many bit errors can be detected?
Error detected!

## Slide 12: Multiple parity bits
11100000010101110101001010001111000
transmit order

## Slide 13: Multiple parity bits
1110000 1 1111000 1
0010101 1 0010101 1
1101010 0 1001010 0
0101000 0 0101010 0
1111000 0 1011000 0
channel
Multiple single-bit errors detected.
transmit order

## Slide 14: Burst errors
1110000 1 0011100 1
0010101 1 0010101 1
1101010 0 1101010 0
0101000 0 0101000 0
1111000 0 1111000 0
channel
Burst error not detected!
transmit order

## Slide 15: Burst errors
1110000 0011100
0010101 0010101
1101010 1101010
0101000 0101000
1111000 1111000
1011111 1011111
channel
transmit order
Burst error detected.

## Slide 16: Checksums
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words.
Example: Internet 16-bit one’s complement checksum.
Properties:
Improved error detection over parity bits.
Detects bursts up to N errors.
Vulnerable to systematic errors, e.g., added zeros.
Q: Disadvantages?

## Slide 17: Checksum Example
add
00000000
11101000
----------- +
11101000
11101000 00100101 11011010 01010000 11111000
transmit order
Internet checksum uses one’s complement arithmetic
Groups of 8 bits  calculate sum mod 256

## Slide 18: Checksum Example
add
11101000
00100101
----------- +
100001101
11101000 00100101 11011010 01010000 11111000
transmit order
Groups of 8 bits  calculate sum mod 256
Internet checksum uses one’s complement arithmetic
(one’s complement arithmetic)
00001110

## Slide 19: Checksum Example
add
00111001
11111000
----------- +
100110001
11101000 00100101 11011010 01010000 11111000
transmit order
Groups of 8 bits  calculate sum mod 256
Internet checksum uses one’s complement arithmetic
00110010

## Slide 20: Checksum Example
add
00111001
11111000
----------- +
100110001
11101000 00100101 11011010 01010000 11111000
transmit order
Groups of 8 bits  calculate sum mod 256
Internet checksum uses one’s complement arithmetic
00110010
11001101
invert

## Slide 21: Checksum Example
11101000 00100101 11011010 01010000 11111000
transmit order
Groups of 8 bits  calculate sum mod 256
Internet checksum uses one’s complement arithmetic
11001101
channel
11101000 00100101 11011010 01010000 11111000
11001101
+
11111111 = 0 (no error)
(one’s complement arithmetic)
Q: Why do we get 0?

## Slide 22: Checksum Example
11101000 00100101 11011010 01010000 11111000
transmit order
Groups of 8 bits  calculate sum mod 256
Internet checksum uses one’s complement arithmetic
11001101
channel
11100000 00100101 11111010 01011000 11111000
10001101
+
11011111 = 223 (error!)
(one’s complement arithmetic)

## Slide 23: Checksum Example
11101000 00100101 11011010 01010000 11111000
transmit order
Groups of 8 bits  calculate sum mod 256
Internet checksum uses one’s complement arithmetic
11001101
channel
11101000 11011010 00100101 01010000 11111000
11001101
+
11111111 = 0 (no error)
(one’s complement arithmetic)

## Slide 24: Cyclic Redundancy Check

## Slide 25: Cyclic Redundancy Check The concept
code word
generator polynomial
errors
0
message
check bits

## Slide 26: Cyclic Redundancy Check Properties and practice
Sender and receiver agree upon polynomial in advance
Example: Ethernet’s 33-bit polynomial is:
CRC is computed with simple shift/XOR circuits
Stronger detection than checksums:
Can detect all double bit errors, odd bit errors
Detect all burst errors bits (in example, )
Not vulnerable to systematic errors
…
Because we use modulo 2 arithmetic.

## Slide 27: Cyclic Redundancy Check

## Slide 28: Cyclic Redundancy Check Example
message: 11010101
generator: 10011
1010000
10011
10000
10011
0011
Message: 11010101, CRC: 0011, Codeword: 110101010011
Modulo 2 arithmetic. No carries/borrows
Q: Consequences for implementation?
0000
1001
Sender adds CRC

## Slide 29: Cyclic Redundancy Check Example
message: 11010101
generator: 10011
1010011
10011
10011
10011
0
Message: 11010101, CRC: 0011, Codeword: 110101010011
Receiver checks for errors
, no error
0011
1001

## Slide 30: Error Correction

## Slide 31: How many errors can we correct?
Consider a code with hamming distance .
We have seen that we can detect single-bit errors.
111000 111111
We can correct errors with changes.
Q: What assumption do we need for this approach to work in practice?
If we receive this value, …
… we assume it should be this value.
But it could have been this value!
Conputer Nrtworls

## Slide 32: Error correction
Hamming codes
Binary convolutional codes
Reed-Solomon codes
Low-Density Parity Check codes
… (many others)

## Slide 33: Multiple parity bits
1110000 1 0010101 0 1101010 0 0101000 0 1111000 0
Error in second row!
receive order

## Slide 34: Multiple parity bits
1110000 0010101 1101010 0101000 1111000 1010111
Error in fourth column!
receive order

## Slide 35: Multiple parity bits
1110000 1 0010101 0 1101010 0 0101000 0 1111000 0 1010111
Error located!
receive order
= Row+column parity bits
= Hamming code

## Slide 36: Hamming codes
Example of an (11, 7) Hamming code correcting a single-bit error.
Minimum number of check bits such that all 1-bit errors can be corrected!

## Slide 37: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 11010101
codeword: __1_101_0101
positions: 123456789…

## Slide 38: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: __1_101_0101
positions: 123456789…
Expand all bit locations into powers of two.
Decide the value of each check bit in position by calculating the parity function over all bits that have in their expansion.

## Slide 39: Hamming codes An example
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000
1 |  |  |  |  | X |  |  | 
2 |  | X |  |  |  |  |  | 
4 |  |  |  |  | X |  |  | 
8 |  |  |  |  |  |  |  | 
The check bit positions
All bit positions
1. Expand all bit locations into powers of two.

## Slide 40: Hamming codes An example
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000
1 | X |  | X |  | X |  | X | 
2 |  | X | X |  |  | X | X | 
4 |  |  |  | X | X | X | X | 
8 |  |  |  |  |  |  |  | X
1. Expand all bit locations into powers of two.

## Slide 41: Hamming codes An example
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000
1 | X |  | X |  | X |  | X | 
2 |  | X | X |  |  | X | X | 
4 |  |  |  | X | X | X | X | 
8 |  |  |  |  |  |  |  | X
Check bit 1 is a parity bit calculated using bits 1, 3, 5, and 7
Check bit 4 is a parity bit calculated using bits 4, 5, 6, and 7
2. Calculate the parity bit using all bits that have in their expansion

## Slide 42: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: __1_101_0101
positions: 123456789…
Position 1+2
Position 4
Position 4+2+1
2. Calculate the parity bit using all bits that have in their expansion

## Slide 43: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: __1_101_0101
positions: 123456789…

## Slide 44: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 1_1_101_0101
positions: 123456789…

## Slide 45: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 1_1_101_0101
positions: 123456789…

## Slide 46: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111_101_0101
positions: 123456789…

## Slide 47: Hamming codes An example
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111110100101
positions: 123456789…

## Slide 48: Hamming codes Error correction
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111111100101
positions: 123456789…
Computer error syndrome:
Check bit 1 = parity of bits 1, 3, 5, 7, 9, 11
Single-bit error

## Slide 49: Hamming codes Error correction
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111111100101
positions: 123456789…
Computer error syndrome:
Check bit 1 = parity of bits 1, 3, 5, 7, 9, 11 = 0
Single-bit error

## Slide 50: Hamming codes Error correction
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111111100101
positions: 123456789…
Computer error syndrome:
Check bit 1 = parity of bits 1, 3, 5, 7, 9, 11 = 0
Check bit 2 = parity of bits 2, 3, 6, 7, 10, 11 = 1
Single-bit error

## Slide 51: Hamming codes Error correction
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111111100101
positions: 123456789…
Computer error syndrome:
Check bit 1 = parity of bits 1, 3, 5, 7, 9, 11 = 0
Check bit 2 = parity of bits 2, 3, 6, 7, 10, 11 = 1
Check bit 4 = parity of bits 4, 5, 6, 7, 12 = 1
Single-bit error
Error at location:
110 (binary)

## Slide 52: Hamming codes Error correction
Use bit-locations that are a power of 2 as check bits. Use the remaining positions for the message.
message: 1 101 0101
codeword: 111111100101
positions: 123456789…
Computer error syndrome:
Check bit 1 = parity of bits 1, 3, 5, 7, 9, 11 = 0
Check bit 2 = parity of bits 2, 3, 6, 7, 10, 11 = 1
Check bit 4 = parity of bits 4, 5, 6, 7, 12 = 1
Single-bit error
Error at location:
110 (binary)

## Slide 53: Convolutional codes
Operates on a stream of bits, keeping internal state.
Output stream is a function of last preceding input bits.
Bits are decoded with the Viterbi algorithm.
Popular NASA binary convolutional code (rate = ½) used in 802.11
… 1 1 1
0 1 1
1 0 1
…
Determines most likely input for given output.
Different from systematic codes and block codes

## Slide 54
0
0
0
0
0
0
Shift registers. Can be initialized with other values
Input
Message

## Slide 55: Message: 1 0 1 Code: …
0
0
0
0
0
0
Input
Message
Output bit 1
Output bit 2

## Slide 56: Message: 1 0 1 Code: 11…
0
0
0
0
0
0
Input
Message
Output bit 1
Output bit 2
1
1+0+0+0+0 = 1
1+0+0+0+0 = 1

## Slide 57: Message: 1 0 1 Code: 1101…
1
0
0
0
0
0
Input
Message
Output bit 2
Output bit 1
0
0+0+0+0+0 = 0
0+1+0+0+0 = 1

## Slide 58: Message: 1 0 1 Code: 110100
0
1
0
0
0
0
Input
Message
Output bit 1
Output bit 2
1
1+1+0+0+0 = 0
1+0+1+0+0 = 0
Q: Are we done dealing with errors?

## Slide 59: Data Link Layer Summary
A1: It depends on the physical medium
Framing (byte stuffing, bit stuffing, etc)
Guaranteed delivery
Sequence numbers, acknowledgments, and retransmissions
Flow control
Stop-and-Wait
Sliding Window
Error control
Detection (e.g., Parity bit, Checksum, CRC, …)
Correction (e.g., Hamming Code, Convolutional Code, …)
Q: When needed?
Q: When needed?
Q: When needed?
A2: It depends on the application
A3: We may want to address the problem in a higher layer
Q: Can you think of an example?