## Slide 1: Computer Networks X_400487
Lecture 11
Chapter 7: The Application Layer—Part 2
Lecturer: Jesse Donkervliet

## Slide 2
The Web provides a common interface to our digital society

## Slide 3: Application Layer Topics
Domain Name System (DNS)
Email
Web (HTTP, QUIC, WebSocket)
Multimedia applications

## Slide 4
HTTP in The World Wide Web

## Slide 5: Hypertext
Vannevar Bush described the Memex, a device for storing data associatively.
The idea existed before digital computers and digital media (e.g., libraries).
Hypertext invented by Ted Nelson and Douglas Engelbart
Vannevar Bush
Ted Nelson
Douglas Engelbart

## Slide 6: The Web TCP+DNS+Hypertext
Tim Berners-Lee, a computer engineer at CERN, started the modern Web by combining TCP, DNS, and hypertext in 1989.
He now directs the World Wide Web Consortium (W3C).
Tim Berners-Lee

## Slide 8: HTTP Request/Response
Physical layer
Data link layer
Medium Access Control
HTML documents hosted by servers. Clients sends request for document from server.
Network Layer
Transport layer
Application layer
HTTP GET
TCP
IP
TCP
IP
HTML document
Web Server
Web browser
Ethernet, 802.11,
…
Ethernet, 802.11,
…

## Slide 9: Evolution of HTTP
Optimizations are gradually incorporated to improve performance/security
1990
1995
2000
2005
2010
0.9
1.0 developed
1.1 developed
(persistent connections)
HTTP 2.0 (SPDY)
Cookies SSL 2.0
RFC 1945
RFC 2068, 2109
RFC 2616
RFC 2965
HTTP/3 (QUIC)

## Slide 10: HTTP Protocol
Originally a simple text-based protocol. Many options added over time.
Try it yourself:
Similar to chat application from the lab!
$ telnet en.wikipedia.org 80
GET wiki/HTML HTTP/1.0

## Slide 11: HTTP Request via TELNET

## Slide 12: HTTP Request Methods
Methods: GET, POST, PUT, HEAD, …
$ curl -v -L --http1.1 https://vu.nl -o /dev/null
…
> GET / HTTP/1.1
> Host: vu.nl
> User-Agent: curl/7.64.1
> Accept: */*
>
…
https://www.w3.org/TR/2010/WD-html5-20100624/
Specifies the protocol, the domain name, and a path.

## Slide 13: Web pages based on Hypertext
HTTP request
HTTP response
youtube.com
w3c.org
google-analytics.com
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 14: Web and HTTP Performance
The Web and HTTP continues to evolve, with servers sending more and larger responses

## Slide 15: Single document
time
HTTP/1.1 GET (e.g., rfc2616)
HTTP response
Connection setup

## Slide 16: Single document Example
https://www.w3.org/Protocols/rfc2616/rfc2616.html

## Slide 17: External resources
HTTP/1.1 GET (e.g., )
HTTP response
time
HTTP/1.1 GET (e.g., vu.nl)
HTTP response
Connection setup

## Slide 18: Server-side programs
time
HTTP/1.1 GET (e.g., canvas.vu.nl)
HTTP responds with personalized page
Connection setup
Server-side program (e.g., PHP, Python)
Page generated at runtime

## Slide 19: Client-side programs
HTTP/1.1 GET (e.g., page refresh)
HTTP response
time
HTTP/1.1 GET (e.g., vu.nl)
HTTP response
Connection setup
Client-side program (e.g., JavaScript)

## Slide 20: Modern webpages Many requests
https://canvas.vu.nl/

## Slide 21: Recap TCP Connection setup
Connection request SYN (seq=x)
SYN, ACK (seq=y, ack=x+1)
ACK (seq=x+1, ack=y+1)
time

## Slide 22: Recap TCP Connection setup
Connection setup
time

## Slide 23: HTTP Sequential requests
time
HTTP request
HTTP response
Connection setup

## Slide 24: HTTP Sequential requests
HTTP request
HTTP response
Connection setup
time
HTTP request
HTTP response
Connection setup
HTTP 1.0

## Slide 25: HTTP Persistent connection
HTTP request
HTTP response
time
HTTP request
HTTP response
Connection setup
Increase performance by reducing connection setup overhead
Persistent connections allow browsers to issue multiple requests over the same TCP connection
HTTP 1.1

## Slide 26: HTTP Performance Problem Head of Line Blocking (HOL)
HTTP request
HTTP response
time
HTTP request
HTTP response
Connection setup
Each request needs to wait for the previous one to complete!

## Slide 27: HTTP1.1 Pipelined requests
HTTP requests
HTTP responses
time
Connection setup
Increase performance by pipelining requests (hiding latency)
Reduces Head of Line Blocking!
Performance problem: Responses need to arrive in same order as requests
HTTP 1.1

## Slide 28: HTTP/2
1. Binary instead of plaintext.
2. Multiplexed streams over a single TCP connection.
3. Server push allows the server to send resources before the client asks for it explicitly.
Easier for machines to parse
More difficult for humans to read
Q: Why would it be easier for machines?
Supports out-of-order responses!

## Slide 29: Head-of-Line Blocking in HTTP/2
Despite pipelining (HTTP1.1) and out-of-order responses (HTTP/2), HTTP/2 performance still suffers from a type of Head of Line blocking
channel
802.11
802.11
IP
IP
Ethernet
Ethernet
TCP
TCP
Internet
HTTP/2
HTTP/2
Data Link
Physical
Network
Transport
Application
Q3
Q2
Q1
R3
R2
R1

## Slide 30: Head-of-Line Blocking in HTTP/2
Despite pipelining (HTTP1.1) and out-of-order responses (HTTP/2), HTTP/2 performance still suffers from a type of Head of Line blocking
channel
802.11
802.11
IP
IP
Ethernet
Ethernet
TCP
TCP
Internet
HTTP/2
HTTP/2
Data Link
Physical
Network
Transport
Application
R1
R3
R2
Q: What happens now?
HOL because TCP delivers data in order

## Slide 31: HTTP/3 (HTTP + QUIC)
HTTP/3 uses the QUIC protocol
QUIC performs multiplexing, uses UDP
channel
802.11
802.11
IP
IP
Ethernet
Ethernet
UDP
UDP
Internet
QUIC
QUIC
Data Link
Physical
Network
Transport
R1
R3
R2
HTTP/3
HTTP/3
Application
Q: What happens now?
UDP does not enforce in-order delivery
QUIC orders data per stream
Each HTTP request can use a separate stream; within a stream, data is delivered in order; across streams no such guarantee is made
RFC 9051

## Slide 32: WebSockets
A socket-like interface on the application layer.
Full-duplex connection between server and client.
Increasingly complex ‘apps’ on the Web that need to send data continuously.
Examples:
irc-ws.chat.twitch.tv
ws.todoist.com
Q: Can you think of a use-case?
Application layer protocol
Q: Can the application layer contain protocols?
RFC 6455

## Slide 33: WebSockets
A socket-like interface on the application layer.
Full-duplex connection between server and client.
Increasingly complex ‘apps’ on the Web that need to send data continuously.
Examples:
irc-ws.chat.twitch.tv
ws.todoist.com
Q: Can you think of a use-case?
‘ws’ stands for WebSocket
Application layer protocol
RFC 6455

## Slide 34: Stacking Application layer protocols
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
TCP
IP
Application
Ethernet, 802.11,
…

## Slide 35: Stacking Application layer protocols
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
TCP
IP
WebSocket
Ethernet, 802.11,
…
Application
Application layer can continue stacking protocols
Protocols may provide services the ones below/above do not!

## Slide 36: Stacking Application layer protocols
Physical layer
Data link layer
Medium Access Control
Network Layer
Transport layer
Application layer
TCP
IP
WebSocket
Ethernet, 802.11,
…
Application
Protocols may provide services the ones below/above do not!
…

## Slide 37: Starting a WebSocket over HTTP
GET /chat HTTP/1.1 Host: example.com:80 Upgrade: websocket Connection: Upgrade Sec-WebSocket-Key: dGhlIHNhbXBsZSBub25jZQ== Sec-WebSocket-Version: 13
HTTP/1.1 101 Switching Protocols Upgrade: websocket Connection: Upgrade Sec-WebSocket-Accept: s3pPLMBiTxaQ9kYGzzhZRbK+xOo=
Client requests to switch to WebSocket protocol
Reply from server if it accepts

## Slide 38: WebSocket frame format

## Slide 39: HTTP is the new “narrow waist”
Method | Description
GET | Read a Web page
HEAD | Read a Web page’s header
POST | Append to a Web page
PUT | Store a Web page
E.g., REST APIs
Provides set of methods
Q: Advantages over using TCP directly?
Provides naming
Provides security
Answers include:

## Slide 40: Application Layer Topics
Domain Name System (DNS)
Email
Web (HTTP, QUIC, WebSocket)
Multimedia applications

## Slide 41: Video dominates
28,000 people watching Netflix
500 hours of content uploaded to YouTube
2 million Twitch views
3.4 million Snaps created
Video constitutes around 70 percent of all global mobile network traffic in 2022

## Slide 42: Streaming Video Requires Compression
1024 height x 2048 width = 2M pixels
1 pixel = 1 byte
30 frames per second  60 MB/s = 480 Mbps
Without compression, only possible over wired fibre-optic channels

## Slide 43: Streaming Video Requires Compression
Compression reduced bandwidth requirement by an order of magnitude

## Slide 44: Digital audio compression
Audio typically compressed before sending.
Lossy compression achieves higher compression rates than lossless compression, but loses data.
Lossy encoders based on how humans perceive sound.
Q: Why is lossy compression acceptable?
Large compression rates .

## Slide 45: Human hearing frequency range

## Slide 46: Human hearing masked signals

## Slide 47: Digital video JPEG compression
Changes to .
is luminance.
are chrominances.
Eyes are less sensitive to chrominance than to luminance.
JPEG reduces size of and . Total compression rate .
Q: Why change to this format?

## Slide 48: Digital video
MPEG compresses over a sequence of frames, further using motion tracking to remove temporal redundancy
I (Intra-coded) frames are self-contained
P (Predictive) Looks for comparable macro blocks in previous frames.
B (Bidirectional) frames may base prediction on previous frames and future frames.
Large compression rates .
Q: What is the use of bidirectional frames?
How long to search is up to the implementation.

## Slide 49: Run-Length Encoding
A lossless compression technique.
Part of JPEG Compression

## Slide 50: Huffman Encoding
“application layer”
61 70 70 6c 69 63 61 74 69 6f 6e 6c 61 79 65 72
(128 bits)
ASCII
Huffman Encoding
String
11 101 101 100 0111 0110 11 0101 0111 0100 0011 100 11 0010 0001 0000
(54 bits)
Less than half the original size!
Prefix code: no code word is prefix of other code word
Q: Why is this useful?

## Slide 51: Huffman Encoding
“application layer”
a
3
a
3
symbol
frequency
p
2
l
2
i
2
c
1
t
1
o
1
n
1
y
1
e
1
r
1
Form a tree by select the two smallest nodes, and combining them into a new node, until only the root is left.
2
2
2
3
4
4
5
7
9
16
1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
11 101 101 100 0111 0110 11 0101 0111 0100 0011 100 11 0010 0001 0000
(54 bits)
Part of JPEG Compression

## Slide 52: Networking Challenges for Multimedia Applications

## Slide 53: Challenge 1 Streaming stored media
How to handle transmission errors?
Use reliable transport (e.g., TCP).
  Increases jitter significantly.
Use forward error correction (error correction in the application layer).
  Increases jitter, decoding complexity, and overhead.
Interleave media
  Slightly increases jitter and decoding complexity.

## Slide 54: Masking errors by interleaving media
Playback on user’s machine
Network
Server
Normal scenario.
Transmission errors.
Transmission errors in interleaved media.
Smaller gaps are less noticeable.

## Slide 55: Challenge 1 Streaming stored media
Low-water mark prevents stalls in playback.
High-water mark gives client time to prevent running out of buffer space.
buffer
V
V
Low-water mark
High-water mark
Provides flow control

## Slide 56: Challenge 2 Streaming live media
Streaming live media is similar to the stored case plus:
Can’t stream faster than live rate to get ahead
  Usually need larger buffer to absorb jitter
Often have many users viewing at the same time
  UDP with multicast greatly improves efficiency. It is rarely available, so many TCP connections are used.

## Slide 57: Challenge 3 Streaming interactive media
Real-time conferencing has two or more connected live media streams, e.g., voice over IP, Skype video call
Requires low jitter and low latency.
Benefits from network support (Quality of Service).
Large bandwidth (no congestion).
Difficult to provide across long distances/multiple networks

## Slide 58: Take-Home Message
Many responsibilies and pseudo layers hidden in Application Layer
  From OSI: Presentation, Session. Others: WebSocket, RTP, etc.
Important behind-the-Scenes applications exist (e.g., DNS)
Traditional “killer apps” for the Internet:
  Email
  The Web
HTTP is the new “narrow waist”
  Improved over time (HTTP/2 [SPDY], HTTP/3 [QUIC])
Today’s Internet is increasingly used for multimedia applications
  Provide new challenges (high bandwidth, low latency, low jitter)